## Slide 1: T-LDP Hello Reduction draft-pdutta-mpls-tldp-hello-reduce-02
Pranjal Dutta
Thomas Nadeau
Giles Heron
draft-pdutta-mpls-tldp-hello-reduce-02
IETF-81

## Slide 2: History
00-version was presented in IETF-74 in MPLS WG
Addressed all feedbacks received from WG in revision -02.
Moved from Informational to Standards Track as per suggestions from MPLS WG.
draft-pdutta-mpls-tldp-hello-reduce-02
IETF-81

## Slide 3: Objectives
Optimize Targeted LDP (T-LDP) session maintenance in scaled T-LDP environment (e.g in mobilility backhauls with Pseudowires/VPLS deployments).
draft-pdutta-mpls-tldp-hello-reduce-02
IETF-81

## Slide 4: Problem Statement
After LDP session establishment T-LDP hellos become redundant. Session Keepalives are sufficient to maintain T-LDP adjacency.
In scaled T-LDP environment , T-LDP Hellos are overheads after the session establishment if BFD etc. are used for tracking neighbor liveliness.
draft-pdutta-mpls-tldp-hello-reduce-02
IETF-81

## Slide 5: Problem Statement
LDP Hellos can cause DoS attacks leading to losing of established adjacencies. It is important to avoid dependency of hellos as far as possible.
draft-pdutta-mpls-tldp-hello-reduce-02
IETF-81

## Slide 6: Procedure
Two T-LDP peering LSRs starts exchanging
T-LDP hellos with “configured” hello timeouts as part of extended discovery.
After LDP session is established, each LSR starts sending Hello Timeout of value 0xFFFF, which is infinite as per RFC 5036.
If both peering LSRs start advertising Hello Timeout of 0xFFFF, then negotiated timeout falls back to 0xFFFF.
draft-pdutta-mpls-tldp-hello-reduce-02
IETF-81

## Slide 7: Procedure
After the LDP session fails, both LSRs start transmitting T-LDP Hellos with the “configured” timeout values again.
draft-pdutta-mpls-tldp-hello-reduce-02
IETF-81

## Slide 8: Benefits
Procedure is very simple and uses existing provisions of RFC 5036 . Backward compatible with LSRs not implementing the procedure.
draft-pdutta-mpls-tldp-hello-reduce-02
IETF-81

## Slide 9: Next Steps
Discussions, feedbacks in PWE3 + MPLS mailing list.
Reach working group consensus on the T-LDP hello reduction mechanism
draft-pdutta-mpls-tldp-hello-reduce-02
IETF-81