## Slide 1: A Unified Control Channel for Pseudowires draft-nadeau-pwe3-vccv-2-02 Thomas D. Nadeau Luca Martini
IETF 81

## Slide 2: Overview
The draft describes a unified control channel for Virtual Circuit Connectivity Verification (VCCV) which could represent VCCV version 2.
Supports all supported access circuit and transport types currently defined for PWs, as well as those supported by The MPLS Transport Profile.
This new mode is intended to update and supersede the capability and operational rules described in RFC5085

## Slide 3: Current Operation and Issues
A variety of VCCV CC and CV types other wise know as "modes" have been created, not only to support current hardware, but to support legacy hardware
The MPLS Transport Profile (MPLS-TP) requirements [RFC5654] require support of VCCV when an MPLS-TP PSN is in use.
  The GAL-ACH had to be created; this effectively resulted in another mode of operation.
The difficulty of operating these different combinations of "modes" have been detailed in an implementation survey the PWE3 Working Group conducted.

## Slide 4: Solution: VCCV 2.0
The draft simplifies the modes of operation of VCCV down to a single mode of operation we refer to as type 4.
This mode simply defines two ways to run VCCV:
  with a control word.
  without a control word, but with a ACH encapsulation making it easy to handle all of the other cases handled by the other modes of VCCV.
In both cases it will be mandatory to implement and use that mode if it is supported, thus simplifying the implementation and operation of the protocol.

## Slide 5: VCCV Capability Advertisement
The capability advertisement MUST match that c-bit setting that is advertised in the PW FEC element.
  If the c-bit is set, indicating the use of the control word, type 1 MUST be advertised and type 4 MUST NOT be advertised. If the c-bit is not set, indicating that the control word is not in use, type 4 MUST be advertised, and type 1 MUST NOT be advertised.
A PE supporting Type 4 MAY advertise other CC types as defined in RFC5085 but if the remote PE also supports Type 4, then Type 4 MUST be used superseding the Capability Advertisement Selection rules of section 7 from RFC5085.
If a remote PE does not support Type 4, then the rules from section 7 of RFC5085 apply. If a CW is in use, then Type 4 is not applicable, and therefore the normal capability advertisement selection rules of section 7from RFC5085 apply.

## Slide 6: Outstanding Issues
Placement of the PW label and GAL have been swapped since last version based on feedback from the mailing list.
How to proceed?
  Do we create a new draft that clearly supersedes RFC5085?
  Do we progress RFC5085 to PS with these changes as updates based on the WG’s and implementation input (i.e.: implementation survey)?
  Adopt this as a WG draft?