## Slide 1: ICCP extension for the MSP application
Presenter: Yuxia Ma
Author: Hongjie Hao
draft-hao-pwe3-iccp-extension-for-msp-00

## Slide 2: Background
Sometimes the SDH and Packet Transport equipments are co-existed in the mobile backhaul network, to achieve a smooth migration from SDH to Packet Transport network. The figure below depicts the scenario.
The Multiplex section protection protocol(MSP) is used to protect the side of UNI.
SDH
SDH
PTN1
BS
PTN2
PTN3
Service Router
MSP
SDH
Notes: An example scenario of mobile backhaul;
Traffic is transported(carried) by one link.
<number>

## Slide 3: Problem statement
The network between PE and CE is SDH network. The PEs and CE run the linear MSP. The PEs need a mechanism to synchronize the state and configuration data between the PEs. ICCP is the exact tool to do the synchronization.
PE2
PE1
CE
Pseudowire
Pseudowire
ICCP
Notes: This is an model abstracted from the above scenario.
There is a cooperation between PW redundancy and MSP protection. It is out of the scale of this draft.
<number>

## Slide 4
ICCP allows synchronization of state and configuration data between a set of two or more PEs forming a RG. It provides reliable message transport and in-order delivery between nodes in a RG with secure authentication mechanisms built into the protocol.
ICCP draft specified the pseudowire redundancy application TLVs and multi-chassis LACP application TLVs. These TLVs are not included the message of MSP application. This draft extends the ICCP TLVs to support the MSP application.
Problem statement (cont)

## Slide 5: The extend TLVs (1)
The draft extends the ICCP TLVs. Multiplex Section Protection (MSP) Application TLVs are :
  MSP Connect TLV
  Establish the MSP application connection
  MSP Disconnect TLV
  Terminate the MSP application connection
  MSP Group Config TLV
  Synchronize the configuration of local protect group, such as group mode, type, WTR time etc.
  MSP Port Config TLV
  Synchronize the configuration of local port, such as role, port name etc.

## Slide 6: The extend TLVs (2)
  MSP Link State TLV
  Synchronize the link state of local node, such as SF, SD
  MSP Switch Command TLV
  Synchronize the local node’s switch command , such as manual switch, forced switch, clear etc.
  MSP Group State TLV
  Synchronize the state of protect group, such as WTR, no request, manual switch etc.
  MSP Synchronization Request TLV
  Request to retransmit the configuration and state
  MSP Synchronization Data TLV
  Response the synchronization request TLV

## Slide 7: Comments from the list
Thanks for the comment from Stewart:
  “The scenario looks similar to Figure 1 in the ICCP draft. Please can you clarify the problem in the ICCP draft that you are addressing.”
Answer
  Figure 1 in the ICCP draft described the generic multi-chassis redundancy model. When the network is SDH network, it is just the situation we talked. But ICCP draft does not specify the MSP application TLVs. This draft extends the TLVs to achieve the MSP application .

## Slide 8: Next step
Looking forward to seeing more comments!

## Slide 9
Thanks