## Slide 1
Dean Cheng (dean.cheng@huawei.com)
81st IETF Quebec City
RADIUS Extensions
for
CGN Configurations
draft-cheng-behave-cgn-cfg-radius-ext-00
1
1

## Slide 2: Motivation
Scenario (in a broadband network)
  User configuration is stored on a RADIUS server (user profile)
  User’s broadband connection terminates at a BNG
  CNG (e.g. NAT44) can be co-located on a BNG
Problem to solve
  How to leverage the existing RADIUS based infrastructure in broadband network to configure & manage subscriber based CGN parameters?
Solution proposed
  Pre-configure the CGN related parameters on the RADIUS server as part of the user profile. This information is propagated to the BNG/CGN by RADIUS messages exchange between BNG and RADIUS server.
  CGN related user parameters are sent from BNG to RADIUS server.
2

## Slide 3: Configure NAT44 TCP/UDP Session Limit via RADIUS
AAA
Server
Access Request
Service Request
NAT44/NAS
BNG
User profile:
Username pwd,
IPv4 address,
CGN TCP/UDP,
Session Limit
Access-Accept
CGN-Session-Limit (TCP/UDP ports)
Service Granted
(other parameters)
User
RADIUS
PPPoE/DHCP
3
Account Request
CGN-Session-Limit (TCP/UDP ports)
(NAT44 external port
allocation and IPv4 address
assignment)

## Slide 4: Change NAT44 TCP/UDP Session Limit via RADIUS
AAA
Server
NAT44/NAS
BNG
User profile:
Username pwd,
IPv4 address,
CGN TCP/UDP,
Session Limit
User
4
TCP/UDP Port Limit (1024)
CoA Request
CGN-Session-Limit (TCP/UDP ports)
TCP/UDP Port Limit (2048)

## Slide 5: CGN-Session-Limit Attribute
Type - TBD
Length – 6 octets
ST (3 bit) -
0: The limit as specified is applied to the sum of TCP ports, UDP
ports and ICMP identifiers.
1: The limit as specified is applied to the sum of TCP ports
and UDP ports.
2: The limit as specified is applied to TCP ports.
3: The limit as specified is applied to UDP ports.
4: The limit as specified is applied to ICMP identifiers.
5-7: Not used.
Reserved – set to zero by sender and ignored by receiver.
Session Limit - This field contains the maximum number that is imposed to the
total number of TCP ports, or UDP ports, or the sum of the two,
or ICMP Identifiers, or the sum of the three, depending on the
value in the Session Type field, that the specific user can use
during CGN operation.
5

## Slide 6: Report NAT44 TCP/UDP Port Allocation Range via RADIUS
AAA
Server
Access Request
Service Request
NAT44/NAS
BNG
User profile:
Username pwd,
IPv4 address,
CGN TCP/UDP,
Session Limit
Access-Accept
Service Granted
User
RADIUS
PPPoE/DHCP
6
Account Request
CGN-Session-Range for de-allocation
CGN allocates a TCP/UDP
port range for the user
Account Request
CGN-Session-Range for allocation
CGN de-allocates a TCP/UDP
port range for the user

## Slide 7: CGN-Session-Range Attribute
Type - TBD
Length – (12 plus the length of Local Session ID) octets
A-bit Flag –
0: The specified range is for allocation.
1: The specified range is for de-allocation.
ST (Session Type) 2 bits:
0: The session range is applied to TCP ports.
1: The session range is applied to UDP port range.
2: The session range is applied to both TCP and UDP port range.
3: The session range is applied to ICMP identifier range.
7

## Slide 8: CGN-Session-Range Attribute (Cont.)
Reserved – set to zero by sender and ignored by receiver.
External Session Range Start:
This field contains the smallest TCP/UDP Port number or the
smallest ICMP identifier number in the session range, which
contains consecutive TCP/UDP ports or ICMP identifiers,
depending on the value of Session Type.
External Session Range End:
This field contains the largest TCP/UDP Port number or the
largest ICMP identifier number in the session range, which
contains consecutive TCP/UDP ports or ICMP identifiers,
depending on the value of Session Type.
External IPv4 Address:
This field contains the IPv4 address assigned to the associated
subscriber to be used in the external realm.
Local Session ID:
This is an optional field and if presents, it contains a local
session identifier at the customer premise, such as MAC address,
interface ID, VLAN ID, PPP sessions ID, VRF ID,etc.The length of
this field equals to the total attribute length minus 12 octets.
8

## Slide 9: NAT44 Port Forwarding Configuration via RADIUS
AAA
Server
Access Request
Service Request
NAT44/NAS
BNG
User profile:
Username pwd
IPv4 address
Internal port
External port
Access-Accept
CGN-Port-Forwarding-Map
Service Granted
(other parameters)
Account Request
CGN-Port-Forwarding-Map
User
(Create a port mapping
for the user, and associate it
with the internal and external
IP address)
RADIUS
PPPoE/DHCP
9

## Slide 10: Change NAT44 TCP/UDP Port Mapping via RADIUS
AAA
Server
NAT44/NAS
BNG
User
10
Internal IP Address
Port Map (a:X)
CoA Request
CGN-Port-Forwarding-Map)
Internal IP Address
Port Map (a:Y))
CoA Response
CGN-Port-Forwarding-Map)
User profile:
Username pwd
IPv4 address
Internal port
External port
RADIUS
PPPoE/DHCP

## Slide 11: CGN-Forwarding-Port-Map Attribute
Type - TBD
Length – Depending on the value of the AF field, the length could be
8, 12 or 24 octets.
AF (Address Family)- 2 bits:
0: no internal IP address
1: The internal address is an IPv4 address.
2: The internal address is an IPv6 address.
3: Unused.
Reserved – set to zero by sender and ignored by receiver.
Internal Port – The internal port for the CGN mapping.
External Port – The external port for the CGN mapping.
Internal IP address – if exists, contains the internal IPv4 or IPv6
address for the CGN mapping.
11

## Slide 12: Next Step …
Solicit review and assistance from RADEXT WG on the RADIUS elements in the draft
Propose as a WG document in BEHAVE WG
12