## Slide 1: RPL industrial applicability statement IETF 81 status
Slide #<number>
IETF 81 – ROLL WG – July 2011
draft-phinney-rpl-industrial-applicability-statement
Tom Phinney
Pascal Thubert
Robert Assimiti
Notes: <number>

## Slide 2: draft Status
Started early June.
Missed 00 date
Tom Phinney, editor
  US Technical Advisor for IEC/SC 65C (http://iec.ch)
  Chair, IEC/SC 65C/WG 1 and IEC/SC 65C/MT
Robert Assimiti, co-author
  ISA100.11a co-editor (http://isa.org)
Pascal Thubert, co-author
  ISA100.11a co-editor
  ROLL/RPL co-editor
Slide #<number>
IETF 81 – ROLL WG – July 2011
Notes: <number>

## Slide 3: What’s specific
Industrial networks evolved concurrent with IP
Process Control and Factory Automation goals differ from those of IT – schism
Need low latency and high cyclic determinism
e.g. ExxonMobil Baytown refinery near Houston (Texas), 100 hectares (40 sq. miles) with 12 control rooms (CRs): 10 refining CRs localized to a few hectares each, 2 CRs that span the plant and interact with the other 10; large chemical plant adjacent to refinery
Largest plants potentially reap the most profit from small productivity improvements, thus are more willing to innovate (in stages) and to fund proven new technology
Slide #<number>
IETF 81 – ROLL WG – July 2011
Notes: ; should allow for reading sensor data from 20 sensors within 10ms.
<number>

## Slide 4: Process control example: a refinery
Sensors and actuator usually close: <100m
  Elements of critical loops can be wire-interconnected
  Low-quality (noisy, intermittent) field power often available
Control room typically 500m to 2km distant
  Wired: power + signal carried together on one twisted pair
    Designed to meet intrinsic safety regulations: ~40mW/pair
    Typically 25-pair to 100-pair wire bundles in buried conduit
  Wireless is most attractive for this long, costly link
    Primary requirement is ≥ 5yr battery life for field devices
    Battery replacement is often very costly or impractical
    Environmental power harvesting strongly desired
Slide #<number>
IETF 81 – ROLL WG – July 2011

## Slide 5: Time-critical process control messaging
Real-time process measurements (value+status): publish/subscribe, published by device on fixed period, subscribed by assigned loop controller(s), which may be local, and by managing devices in remote control room(s)
Real-time loop controller outputs (value+status): also pub/sub, similar to process measurements
  Together these last two imply that controllers drive actuators while actuators report their state back to the same controllers
Process alarms, network and device alerts: source/sink, multicast to managing devices in remote control room(s)
Control room commands to field devices: peer/peer
Slide #<number>
IETF 81 – ROLL WG – July 2011

## Slide 6: Publish/subscribe communications
Used as interconnect for closed-loop control
Control algorithms are designed to ride through loss of 1-3 successive periodic pub/sub reports
Loss of four successive periodic pub/sub reports not acceptable:
  Causes actuator to go into a fallback control mode
  Considered a system failure by the plant operator
  For the Baytown example, should happen less than once/year across the entire refinery
Slide #<number>
IETF 81 – ROLL WG – July 2011

## Slide 7: Loss mitigation strategies for wireless
For wireless pub/sub:
  Use peer/peer to line-powered router (usually a BR), which takes over any pub/sub multi-destination needs
  Keep devices 1 hop from BR except under failure
  Retry: Wireless 95% per-message success rate implies up to 7 retries needed for any given message
  Use duocast (send once, two scheduled receivers):
    Changes per-xmt success statistic from 95% to 99.75%
    Reduces the above to 3 retries max, easing scheduling
  As a last resort, use wire for critical local interconnect
Slide #<number>
IETF 81 – ROLL WG – July 2011

## Slide 8: Optimized vs. ad-hoc routing
1980: Exxon used supercomputers of the era for continuous time-critical control loop optimization
For critical control, optimized routing can double network performance vs. ad-hoc
Critical control impacts directly how much profit is extracted from raw materials (e.g. barrel of oil)
Centralized optimization can use existing plant databases and actual pairwise attenuation/fading as measured in-situ by operating devices
Slide #<number>
IETF 81 – ROLL WG – July 2011
Notes: Reconciling RPL’s locally independent operation (discovery, maintenance, RIPPLE algorithm) with the deterministic, centralized management and paradigm according to which process automation wireless networks are managed
Battery considerations – how does discovery and maintenance of DODAG and routes affect the life of the battery life which as all of you know, is crucial in process automation instrumentation
Local and global DODAG repair -> route integrity and a continuous guarantee of path diversity is crucial for process automation wireless field devices given that various latencies (typically quite strict) need to be guaranteed
<number>

## Slide 9: RPL applicability
RPL coexists with optimized routes, for construction of initial suboptimal routes and for repair of optimized routes
RPL is adequate for non-production phases (unit startup and shutdown), for emergency rerouting, for non-critical applications, for small plants
Mobile devices (e.g., cranes) may need RPL
When using a reference (optimized) DODAG version from a centralized computer, RPL would provide local repair
Slide #<number>
IETF 81 – ROLL WG – July 2011
Notes: For each flow: Service class: 0-5, per RFC5673, 3.1 [Note: 3 bits suffices] [0=Emergency action; 1=Closed-loop regulatory control; 2=Closed-loop supervisory control; 3=Open-loop control; 4=Alerting; 5=Logging and downloading / uploading] Periodicity: Periodic, Cyclic, Acyclic [Note: 2 bits suffices for specifying the class] for Periodic: Period: 1-250 ms, 1-250 0,25 s intervals, 1-250 min Max permissible delivery jitter (% of period to 200%) Mean fraction of periodic transmission slots used (%) [Note: 3 bits should suffice] for Cyclic: Min repetition interval: 1-250 ms, 1-250 0,25 s intervals, 1-250 min Max permissible transmission jitter (% of min repetition interval to 200%) Mean fraction of cyclic transmission slots used (%) [Note: 8 bits should suffice, in 0,5% increments] for Acyclic: Min expected repetition interval: 1-250 ms, 1-250 0,25 s intervals, 1-250 min Max permissible transmission jitter (% of min expected repetition interval to 200%) /* Note: If the concept of a mean applies, the flow is cyclic, not acyclic. */ Importance (relative to most flows with same service class and period): ++ / + / 0 / - [Note: 2 bits suffices] Communication class: peer-to-peer (P2P), publish-subscribe (P2MP), source-sink (MP2MP) [Note: 2 bits suffices] /* Note: In most cases, P2MP is to a single destination, and MP2MP is to a redundant set of logically equivalent destinations. Intermediary N-cast may be used for either. */
<number>

## Slide 10: Bootstrapping / Link mgt
ISA100.11a, WirelessHART, WIA-PA provide secure bootstrap, so a device can find a parent
control channel? Default, provisioned before or at device installation, initial low capacity; at link level this is ‘out of the box’
Comm moves rapidly to secure, alternate, scheduled control channel via OTA provisioning
Then RPL can play over the control channel
TDMA channel/slot allocation is ‘chicken & egg’
Slide #<number>
IETF 81 – ROLL WG – July 2011

## Slide 11: Why go wireless?
Better process optimization and more accurate predictive maintenance increase profit; 1% improvement in a refinery with a $1.5B annual profit leads to $40k/day ($15M/yr) more profit
Thus more and different sensors can be justified economically, if they can be connected
But wire buried in conduit has a high installation and maintenance cost, with long lead times to change, and is difficult to repair
The solution: wireless sensors in non-critical applications, designed for the industrial environment: temperature, corrosion, intrinsic safety, lack of power sources (particularly when there is no wire)
For critical control loops, use wireless control room links with controllers located in the field, possibly connected over local wiring
Slide #<number>
IETF 81 – ROLL WG – July 2011

## Slide 12: Wireless BRs
4Hz and 1Hz are common rates for primary process control loops
When most high-rate wireless devices are 1 hop from a BR, the BRs are transmitting or receiving during most communications
Duocast, which requires two receiving BRs, increases that load
Antenna placement for collocated BRs is problematic, due to the need to separate the antennae to avoid the near/far problem, where receiver front-ends overload from any nearby transmission
  Real process environments have few places to mount a BR antenna
Thus a low-cost high-capacity multi-channel shared-antenna BR (which also shares LNA and PA) makes enormous sense
  However, such a multi-channel BR can't transmit on any channel while receiving on others (due to the near/far problem)
  Requires co-scheduling of channels and alignment of time slots in which the BR is active, including alignment of potential Acks in those time slots
Slide #<number>
IETF 81 – ROLL WG – July 2011

## Slide 13: Evolution
Multiple link types, optimized for minimal energy and interference at varying degrees of per-trial communication success
Would use FEC selectively when links support it
Might adjust xmit power (e.g. emergency safety message within 1s; required by law)
Different operating tradeoffs use different OF
RPL separates links by OF/constraints/colors
Slide #<number>
IETF 81 – ROLL WG – July 2011