## Slide 1: A Mechanism to Measure the Quality of a Point-to-point Route in a Low Power and Lossy Network draft-ietf-roll-p2p-measurement-01
Mukul Goyal
University of Wisconsin Milwaukee

## Slide 2: Introduction
When an existing route to a destination is not satisfactory, a router can use P2P-RPL mechanism to discover a better route.
P2P-RPL route discovery requires the specification of routing constraints that the discovered route must satisfy.
Thus, the router may need to determine the aggregated values of the routing metrics along the existing route and use this knowledge to frame reasonable routing constraints for use in P2P-RPL route discovery.
The route to be measured can be a source route or a hop-by-hop route established using RPL or P2P-RPL.

## Slide 3: Functional Overview
The origin sends a Measurement Request along the route to be measured.
The Measurement Request accumulates the values of the routing metrics as it travels towards the target.
Upon receiving the Measurement Request, the target unicasts a Measurement Reply, carrying the accumulated values of the routing metrics, back to the origin.

## Slide 4: The Measurement Object (MO)

## Slide 5: The Measurement Object
Serves as both Measurement Request and Measurement Reply
An MO consists of the following fields:
  RPLInstanceID: Relevant only if the MO travels along a hop-by-hop route.
  SequenceNo: Uniquely identifies a Measurement Request and the corresponding Measurement Reply.
  Compr: Indicates the number of prefix octets that are elided from the IPv6 addresses in Origin/Target Address fields and the Address vector.
  Type (T): Indicates whether the MO represents a Measurement Request or a Measurement Reply.
  Hop-by-hop (H): Set if the MO travels along a hop-by- hop route identified by the RPLInstanceID and, if required, the Origin Address serving as the DODAGID.
    In case the P2P route being measured lies along a non-storing DAG, an MO may travel along a hop-by- hop route till the DAG's root, which then sends it along a source route to its destination. In that case, the DAG root will reset the H flag and also insert the source route to the destination inside the Address vector.

## Slide 6: The Measurement Object
  Accumulate Route (A):
    Relevant only if the MO is a Measurement Request that travels along a hop-by-hop route represented by a local RPLInstanceID.
    Indicates if the Measurement Request MUST accumulate a source route for use by the target to send the Measurement Reply back to the origin.
  Reverse (R):
    Relevant only if the MO is a Measurement Request that travels along a source route, specified in the Address vector.
    Indicates if the Address vector contains a complete source route from the origin to the target, which can be used, after reversal, by the target to source route the Measurement Reply message back to the origin.
  Num:
    Indicates the number of fields in the Address vector.
  Index:
    If the Measurement Request is traveling along a source route , this field indicates the index in the Address vector of the next hop on the route.
    If the Measurement Request is accumulating the reverse route, this field indicates the index in the Address vector where the next address must be stored.

## Slide 7: The Measurement Object
  Origin Address:
    An IPv6 address of the origin. Also indicates the DODAGID if the MO travels on a P2P-RPL route. Compr number of prefix octets elided.
  Target Address:
    An IPv6 address of the target after eliding Compr number of prefix octets.
  Address[1..Num]:
    A vector of IPv6 addresses (with Compr number of prefix octets elided) representing a (partial) route from the origin to the target
  Metric Container Options:
    An MO MUST contain one or more Metric Container options to accumulate routing metric values for the route being measured.