## Slide 1: Identifying Defunct DAGs in RPL draft-goyal-roll-defunct-dags-00
Mukul Goyal
University of Wisconsin Milwaukee

## Slide 2: Main Idea
Need a mechanism that allows a node to identify defunct DAGs and delete the state it maintains for such DAGs.
Specify a “no inconsistency” flag inside a DIS.
With “no inconsistency “ flag set, a multicast DIS would not lead to the reset of trickle timers in the receiving RPL routers.
Same mechanism specified in draft-dejean-roll-selective-dis-00 (“Selective DIS for RPL”)
Plan to merge the two documents

## Slide 3: When does a node remove a neighbor from the parent set for a DAG?
When the DAG’s life time is over.
When the neighbor is no longer reachable
When the neighbor advertises in its DIO an infinite rank in the DAG
When keeping the neighbor as a parent would required the node to increase its rank beyond L+DAGMaxRankIncrease
  L is the minimum rank the node had in the DAG
When the neighbor advertises in its DIO membership in a different DAG within the same RPL Instance, where a different DAG is recognized by a different DODAGID or a different DODAGVersionNumber.

## Slide 4: A node may fail to remove a neighbor from parent set
The node fails to receive the neighbor's DIOs advertising an increased rank or the neighbor's membership in a different DAG
The node may not check the neighbor's unreachability for a long time.
  RPL is proactive, hence the lack of data traffic using a DAG can not be considered a reliable indication of the DAG's defunction.
  Trickle timer based control of DIO transmissions means the possibility of an indefinite delay in the receipt of a new DIO from a functional DAG parent.
In such cases, a node would continue to consider itself attached to a DAG even if all its parents in the DAG are unreachable or have moved to different DAGs.

## Slide 5: Need a mechanism to identify defunct DAGs
Using unicast DIS to query individual parents may be expensive.
Hence, the mechanism specified in this document is based on the use of a multicast DIS message to solicit DIOs about a DAG suspected of defunction.
As per RPL specs, receipt of a multicast DIS is treated as an inconsistency and causes the reset of Trickle timer.

## Slide 6: No Inconsistency Flag in DIS
On receiving a unicast/multicast DIS with N flag set,
  an RPL node MUST NOT reset the trickle timers for the DAGs that match the DIS predicates.
  For each DAG matching the predicates of a multicast DIS, an RPL node MUST schedule a DIO transmission after a time duration between Imin/2 and Imin, where Imin is the minimum Trickle interval size
  For each DAG matching the predicates of a unicast DIS received with N flag set, an RPL node MUST immediately generate a DIO.

## Slide 7: draft-dejean-roll-selective-dis
“No Inconsistency” flag is same in operation as “Leaf Node” flag proposed in draft-dejean-roll-selective-dis
Nodes responding to a DIS with “Leaf Node” flag set MUST send a unicast DIO
  Unicast DIO MUST include a Configuration option.
draft-dejean-roll-selective-dis defines a “Response Spreading” option that specifies the time interval over which the DIO responses must be spread.

## Slide 8: Identifying A Defunct DAG
When an RPL node has not received a DIO from any of its parents in a DAG for more than MaxSilence*Imax seconds
  The node MUST generate a multicast DIS message that carries a Solicited Information option and has N flag set.
  The Solicited Information option MUST have the I and D flags set and the RPLInstanceID/DODAGID fields MUST be set to values identifying the DAG.
  The V flag inside the Solicited Information option SHOULD NOT be set so as to allow neighbors to send DIOs advertising the latest version of the DAG.
  After sending the DIS, the node MUST wait for Imin duration to receive the DIOs generates by its neighbors.

## Slide 9: Identifying A Defunct DAG
  At the conclusion of the wait period:
    If the node has received one or more DIOs advertising newer version(s) of the DAG, it MUST join the latest version of the DAG, select a new parent set among the neighbors advertising the latest DAG version and mark the DAG status as functional.
    Otherwise, if the node has not received a DIO advertising the current version of the DAG from a neighbor in the parent set, it MUST remove that neighbor from the parent set.
    As a result, if the node has no parent left in the DAG, it MUST
      mark the DAG as defunct
      schedule the deletion of the state it has maintained for the DAG after DAGHoldTime duration.
  An RPL node SHOULD check the functional status of a DAG it belongs to at least once every CheckDAGStatusTime interval