## Slide 1: The Case for Layered Codecs
Stephan Wenger Alex Eleftheriadis

## Slide 2: Limitations to presentation
Emphasis here on Video (similar constraints may or may not apply to other media)
Emphasis on UDP-based media distribution, implying required error resilience in the source coding
  Making the bold assumption that people here understand and agree that transport-based repair alone does not fulfill real-time requirements

## Slide 3: Need for Error Resilience
Prediction chain between pictures
When broken, bad things happen
Can’t easily use (naïve) re-transmission: adds too much delay
Can’t use Intra pictures
  Too big, adds too much delay
  Too vulnerable, because they are too big
P
P
P
P
I

## Slide 4: Video Error Resilience Tools
Intra Pictures (bad)
Intra MB walk-around (works, but bad experience and inefficient)
Reference picture selection based on feedback (NEWPRED, or more sophisticated, periods of bad pictures, efficient, but makes complex system assumptions, non-trivial for multi-party scnearios)
Temporal Scalability (reference picture selection, multithread, works, quite efficient especially with retransmission, avoids retransmission-delay)
Spatial Scalability
  Adds sophisticated technology for bandwidth adaptation
  Allows efficient support of use case requiring multiple resolutions (picture resize, thumbnail, etc.)

## Slide 5: Temporal Scalability
Inherently more error resilience than IPPP coding (green pictures can be lost without negatively affecting prediction chain)
Allows for re-transmission of lost (blue) P pictures due to larger time intervals
Supported by VP8 in conjunction with newest RTP payload draft
P
P
I
P
P
P

## Slide 6: Spatial Scalability (vs. Simulcast)
Simulcast: send multiple resolutions of the same content
  Can use all tools mentioned before, including temporal scalability
Spatial Scalability: add inter-layer prediction (green arrows)
  Neutral in terms of computational complexity
  Layering reduces sending bitrate, can increase receiving bitrate
  Allows bandwidth adaptation beyond QP adjustment
  Enables efficient implementation of user experience (some use cases)
    Per-user layout in multipoint without transcoding MCUs
    Straightforward support of heterogeneous receiver population
To support spatial scalability, one needs a modern video coddec (for example H.264 SVC)
P
P
P
P
I
P
P
P
P
I

## Slide 7: Thank You