## Slide 1: RTP Functionalities for RTCWEB
A combined view from the authors of draft-cbran-rtcweb-media-00
draft-perkins-rtcweb-rtp-usage-02

## Slide 2: Introduction
Agreement that RTP is the protocol choice for Real-time Media Transport.
These slides walk through the proposed set of RTP features
  Provide a short motivation and explanation
  The proposed requirement level for Implementation in an RTCWEB end-point for each
  There is no discussion of RTP multiplexing in these slides
Open Issues:
  RTP Retransmissions level of requirement
  Forward Error Correction, method and requirements level
  Bit-rate Adaptation Solution

## Slide 3: Core Featuers
RTP [RFC3550] is REQUIRED
RTCP is REQUIRED
SAVPF RTP Profile [RFC5124] is REQUIRED
  Secure RTP provided
  AVPF RTCP Transmission rules
    Timelier transmission of events
    More efficient usage of RTCP bandwidth
Key-management for SRTP, most talked about candidate is DTLS-SRTP [RFC 5764]

## Slide 4: RTP Optimizations
RTP and RTCP Multiplexing [RFC5761] is REQUIRED
  Multiplex RTP and RTCP on one lower layer identifier
Reduced Size RTCP [RFC5506] is REQUIRED
  Allows one to send RTCP packets that are not compound packets as specified in RFC3550
  Improves RTCP performance when sending feedback events
Symmetric RTP [RFC4961] is REQUIRED
  Send RTP and RTCP in bi-directional flows within an RTP session
Short-term persistent RTCP CNAME Generation (method B) [RFC6222] is RECOMMEND
  High Quality CNAME identifiers
  Preserves privacy

## Slide 5: Conferencing Extensions
The extensions improves centralized conferencing
Full Intra Request (FIR) [RFC5104] is RECOMMEND
  Used by centrla nodes to request a new Intra to facilitate switch or when a new user joins the session.
Picture Loss Indicator (PLI) [RFC5104] is RECOMMENDED
  Sent by end-points that are missing packets resulting in corrupted decoder state
Temporary Maximum Media Stream Bit Rate Request [RFC5104] is RECOMMEND
  Allows a central node or end-point to request a temporary cap in media bit-rate from a particular source.
  Facilitates adaptation across central nodes

## Slide 6: RTP Header Extensions
RTP Header Extension provides Meta Data about media stream
If any header extension is implemented [RFC5285] is REQUIRED
  Core specification for extensible and stackable header extensions
Rapid RTP Synchronization [RFC6051] is RECOMMENDED
  The header extension allows RTP synchronization information also carried in RTCP to be sent with media stream at e.g. start up or when new end-point joins a conference
Client to Mixer Audio Level [draft-ietf-avtext-client-to-mixer-audio-level] is RECOMMEND
  Allows a mixer to make selection decision based on this header, rather than decoding audio and measuring audio levels
Mixer to Client Audio Level [draft-ietf-avtext-mixer-to-client-audio-level] is OPTIONAL
  Clients receiving a mixed audio stream gets indication of level for the ones included in the mix. Thus allowing GUI indications.

## Slide 7: Open Issue: RTP Retransmission
RTP Retransmission [RFC4588] is an RTP packet loss repair mechanism:
  Allows for selective retransmissions, i.e. focus on intra frames or preserving prediction chains
  Very bandwidth efficient
  Down side is extra delay it adds between transmission and when media decoding can start
    Usable in interactive communciation within continents
    Ericsson has good practical experience using it in centralized video conferencing
  Error free media at lower base quality prefered over erronous at higher base quality
  Targets correcting packet loss rates up to ~5%
    Bit-rate adaptation should prevent high persistent loss rates
What level of Implementation Requirement should it have?
  RECOMMENDED
  OPTIONAL

## Slide 8: Open Issue: Forward Error Correction
Forward Error Correction (FEC) is an alternative to retransmission (RTX)
Possible to reduce delay compared to RTX, but has more overhead.
  Additional delay allows for reduction in overhead
Possible Solutions
  Basic redundancy [RFC2198] (audio and text only), or using the retransmission format [RFC4588]
  XOR based Block FEC [RFC5109]
  Block FEC Schemes, e.g. Reed-Salomon [draft-galanos-fecframe-rtp-reedsolomon-03] or Raptor [draft-ietf-fecframe-rtp-raptor-04]
Potential IPR Concerns
What to select, if any, is an Open Issue!

## Slide 9: Open Issue: RTP Rate Control
A Clear Need for RTP Media Rate Control:
  Hetrogenous paths require that, at minimum, one prevents self-induced congestion
  Avoiding filling buffers also keeps latency low
  Some level of resource sharing is likely good:
    TCP Friendliness is not required
The open issue is the lack of a standardized, implemented and tested solution
Possible Solutions are:
  TFRC for RTP [draft-gharai-avtcore-rtp-tfrc-00]
  RTP over DCCP [RFC 5762] using CCID=3 (TFRC) [RFC 5762] or CCID=4 (TFRC-SP) [RFC 5622]
  ?