## Slide 1: An Architecture for IP/LDP Fast-Reroute Using Maximally Redundant Trees draft-atlas-rtgwg-mrt-frr-architecture-00
Alia Atlas, Maciek Konstantynowicz (Juniper Networks)
Gábor Enyedi, András Császár (Ericsson)
Russ White, Mike Shand (Cisco Systems)
IETF 81, Quebec City, Canada

## Slide 2: Outline
Motivation
Architecture
Algorithm
Next Steps

## Slide 3: LFA isn’t enough…
LFA is useful and networks are being designed to improve coverage (draft-ietf-rtgwg-lfa-applicability)
…but LFA doesn’t guarantee 100% coverage.
NotVia can guarantee coverage but requires significant network state
  Research done to reduce it, but nothing sufficiently practical & it’s been years
Increasing Requirement and Demand for IP/LDP Fast-Reroute with 100% Coverage

## Slide 4: Unicast isn’t enough…
Multicast is increasingly deployed and needs protection…
  Need live-live as well as fast-reroute
Need to consistently cover each case. *
* Still working on SRLG Protection ideas

## Slide 5: What if…
We can always* compute two link and node disjoint paths between any two routers?
The primary neighbor (N) may be on at most one of the red path from S to D or the blue path – but guaranteed* not both.
Recent Research tells us how:
  Compute destination-routed Maximally Redundant Trees
We can plug-n-play different algorithms into this architecture.
Avoids failure-specific paths to reduce state compared to NotVia
* If network doesn’t have other path (e.g. not 2-link or 2-router connected), compute the most disjoint (e.g. maximally redundant) possible based on the network.
E
D
R
C
A
B
F
G
I
J

## Slide 6: Maximally Redundant Trees (MRTs)
Compute a pair of disjoint MRTs per IGP-area destination (e.g. router or multi-homed prefix).
Trade-offs with algorithm between speed and length (not existence) of path. Can compute complete MRTs or just next-hops.
  An algorithm exists that allows a router to compute its next-hops on each pair of MRTs for each node in the network in O( e ) time.
  Algorithms designed to work in real networks:
    Just as with SPF, algorithm is based on a common network topology database – no messaging is required.
    MRTs are computable when network isn't 2-edge or 2-vertex connected – most disjoint paths are computed.
    Need to define consistent tie-breakers to ensure identical destination-rooted MRTs computed by all routers in IGP area.
E
D
R
C
A
B
F
G
I
J
Two maximally redundant
blue/red trees rooted at node R

## Slide 7: Usability Goals for the new IPFRR scheme
Ensure maximum link and node disjointness for any topology
Automatically compute backup next-hops based on the link-state database.
Do not require any signaling in case of failure, use pre-programmed backup next-hops
Introduce minimal additional addressing and state on routers
Enable phased deployment and backward compatibility
Do not impose requirements for external computation
Handle real networks – that may not be fully 2-connected, due to previous failure or design. This also helps with phased deployment.

## Slide 8: Using MRT Alternates for Unicast
MRTs supplement LFAs and do not replace them.
  Compute normal SPT and per-IGP-area-destination Blue & Red MRTs.
  Pre-compute whether Blue MRT or Red MRT will survive primary next-hop failure & select which to use.
    Work-in-progress: doing this quickly for the fast algorithm that computes only next-hops
  In case of a failure:
    If a node-protecting LFA exists, use it.
    Otherwise, if only link-protection is needed and there is a link-protecting LFA backup, use it.
    Otherwise, use the pre-selected MRT, whether Blue or Red.

## Slide 9: Unicast Forwarding: For Want of 2 bits…
IP unicast – tunneling is the only option
  Each router supporting MRT would need to announce two additional loopbacks associated with MRT colors
  Transit MRT routers would use these addresses to identify MRT topology to forward traffic along
  LDP tunneling as alternative
LDP unicast – two alternatives
  (1) topology-id labels
    Specify two additional labels, one per MRT color
    Stack topology-id label on top of LDP FEC label
    When sending packet on MRT, 1st swap FEC label, then push MRT label. Every hop, pop MRT label, swap FEC label, and push MRT label.
  (2) topology encoded in labels
    Routers would need to provide two additional labels per FEC, identifying MRT color
  No new hardware capabilities needed – basic MPLS or context-label spaces.

## Slide 10: Multicast Live-Live with MRTs
Use MRTs rooted at the Multicast Source
Extend PIM and mLDP to indicate which topology (e.g. blue or red MRT) to use for the multicast tree.
Receivers join both the blue MRT and red MRT to receive traffic.
As in draft-karan-mofrr, receivers determine which packets to keep.
Work-in-Progress: Packets may need to identify their topology/tree for non-2-connected networks. (e.g. if a common link must be used)

## Slide 11: Multicast and Fast-Reroute: Basic Issues
Several basic issues with FRR for multicast
  PLR does not know the set of next-next-hops in the multicast tree
  For mLDP, the PLR doesn’t know the right labels to use for the next-next-hops in the multicast tree
  MP does not know upon what interface to expect backup traffic.
Basic Protocol Extensions needed
  Extend PIM Join Attributes and mLDP to specify the router’s next-hops on the multicast tree.
  Extend mLDP to provide the advertised labels for the router’s next-hops.
  Either explicitly signal Upstream Backup Joins or tunnel packets so MP knows packets are from alternate.

## Slide 12: Multicast Traffic Handling
When PLR detects a failure, it doesn’t know if it is a link failure or a node failure.
  For unicast, always send on a node-protecting alternate.
  For multicast, send traffic on both a node-protecting alternate and a link-protecting alternate. The primary neighbor may have receivers too!
  PLR sends traffic on alternates for a configurable time-out.
MP can independently determine whether to accept alternate traffic.
  If primary upstream link is up, keep accepting traffic via that.
    Either failure hasn’t happened or
    Link failure happened and upstream neighbor is getting and forwarding traffic on alternate.
  Otherwise, accept and forward alternate traffic.
  When traffic is received on a new primary upstream link, stop accepting and forwarding alternate traffic.
  Work-in-progress: For mLDP, need to consider all direct links to upstream.

## Slide 13: Where to Replicate? At PLR??
PLR can use unicast alternates to the primary neighbor and next-next-hops.
  Replicate at PLR
  Tunnel multicast traffic in unicast (either IP or LDP) where the outer IP address or LDP label indicates the MP and the appropriate topology (SPT, blue MRT or red MRT).
MP recognizes that traffic is via alternate because it comes in tunneled with MP as destination.
  Could use explicit NULL or a known label for LDP.
Standard issues with ingress replication
  Same packet may be duplicated many times on a link.
Requires tunneling of traffic.

## Slide 14: Where to Replicate? Along alternate-tree?
PLR knows its alternate (preserve independence of selection) – so needs to originate the Upstream Backup Joins.
  Separate messages unicast destined to each MP
  Indicate MP and topology (SPF, blue MRT, red MRT) to use.
  Backup tree is the merged set of unicast alternates.
    E.g. Alternate to E might be LFA, alternate to F might be on a blue F-rooted MRT, and alternate to G might be on a red G-rooted MRT.
Need to merge alternate-trees from different PLRs for same (S,G).
  Drawback is unnecessary replication
To reduce state, could merge alternate-trees from different PLRs for same S.
  Same candidates for next-next-hops

## Slide 15: Cntd. Where to Replicate? Along alternate-tree? Merging Alternate-trees from different PLRs
D can’t tell if a packet from C should go on orange alternate tree or on purple alternate tree.
Merge the alternate-trees.
MPs know which traffic to keep or discard – so just use bw on alternate-tree links.
Less state and simpler.

## Slide 16: Cntd. Where to Replicate? Along alternate-tree? Multicast Primary Tree and Alternate-Tree intersect
D can’t tell if a packet should go on the primary tree or on the alternate-tree.
Need to mark traffic in alternate-tree as being alternate.
  LDP topology-id label
  Different multicast address (and rewrite at MPs)
  Other ideas??

## Slide 17: Work in Progress
Important Practical Problems:
  An ABR may need to know about 2 MRTs per area (and the packet may need to indicate the area). How can we reduce this state?
  Details on how to handle multi-homed prefixes.
Protocol Work to Do:
  OSPF, ISIS, PIM, LDP, mLDP
  Capability advertisements and Management Controls

## Slide 18: Algorithmic Work In Progress
  Define rules and behavior for broadcast interfaces (straightforward).
  Pre-compute, when only MRT next-hops are known, which MRT won’t fail with primary neighbor.
  Administratively Unavailable Links and Nodes
  Asymmetric Link Costs
  Tie-breaking rules
  Specification of using multiple next-hops (like ECMP) in MRTs
  Complete specification of fast-compute MRTs algorithm
  Complete specification of better-paths MRTs algorithm
  How to build MRTs that are SRLG-disjoint?

## Slide 19: Outline
Motivation
Architecture
Algorithm
Next Steps

## Slide 20: Finding MRT
Key: special partial order is needed
  Can be represented by a directed graph
    Almost Directed Acyclic Graph
    Remove the root of it to convert it into a DAG
root
a
b
e
d
c
root<a<b<c<d<root
b<e<d

## Slide 21: Why is it good?
Use an increasing and a decreasing path
  They are disjoint!
  Combine them, and you get two trees
root
a
b
e
d
c
Combine them in any way, they are disjoint on path from node to root

## Slide 22: Load sharing?
You can even vary the next hop
  You can do load sharing like ECMP
root
a
b
e
d
c

## Slide 23: Creating a partial order (ADAG)
Find a path
  Between two vertices already in the order
  Using only vertices not in the order
  Add it in a direction, which keeps up current order
root
a
b
e
d
c
root<a<d<root

## Slide 24: Creating a partial order (ADAG)
Find a path
  Between two vertices already in the order
  Using only vertices not in the order
  Add it in a direction, which keeps up current order
root
a
b
e
d
c
root<a<b<c<d<root

## Slide 25: What is with the first path?
Find a path from the root to the root
  Actually, that is a cycle… 
root
a
b
e
d
c

## Slide 26: Short vs. Fast?

## Slide 27: Technology has matured
Very well studied area (at least 20-30 papers)
Various optimizations for
  Sensor networks
  Optical networks
Works based on link state database
Finding 3/4 trees in 3-/4-connected networks
Algorithm complexity less than SPF
Goal: Find the best trade-offs for an algorithm in
real networks.

## Slide 28: Next steps
Continue work
Get feedback on preferred trade-offs
Interested in becoming a RTGWG draft
  Good starting point with architecture
Questions & Comments?