## Slide 1: MPLS Fast Re-route using extensions to LDP
draft-kini-mpls-frr-ldp-01
Authors: Sriganesh Kini & Srikanth Narayanan
IETF 81 Quebec City, July 2011

## Slide 2: Motivation and Goal
LDP LSPs are widely deployed.
Goal of sub 50msec recovery for traffic on routed paths (IGP shortest path)
Full coverage needed
Solution should be self-contained. It should be independent of other protocols and mechanisms such as IP-FRR, RSVP-TE, IGP convergence etc

## Slide 3: Solution characteristics
Local repair mechanism
  Computation intensive tasks are performed much before the actual failure (during steady state).
  Only PLR reacts to the failure trigger to recover the traffic
  Actions at the PLR to recover the traffic are simple (and pre-computed)

## Slide 4: Solution summary
Defined for link-state IGP. And for platform label space.
Backup shortest path (BSP) LDP LSP setup before failure whenever LFA does not exist
BSP LSP starts at PLR and merges into shortest path LDP LSP tree. Merge point referred to as BSP-MP.
Fast re-route action on detecting failure
  PLR label switches to pre-selected BSP LDP LSP
  Stack label to aggregate failures. Use shortest-path LSP from PLR to BSP MP whenever possible.

## Slide 5: Computation
SPT for a destination
Failure at PLR
Nodes upstream of failure in the SPT is affected
Nodes not upstream of failure in the SPT is not affected
Compute SPT with “failure” excluded – Exclude-SPT
Alternate path from PLR to destination in Exclude-SPT merges back into SPT @ BSP-MP (not upstream of failure)
BSP LSP from PLR to BSP-MP protects the traffic under failure

## Slide 6: SPT & Exclude-SPT
S1
S2
P
D
M
S1
S2
P
D
M
S1
S2
P
D
M
Topology
SPT
Exclude-SPT
M
D
P
S2
M
D
P
S2
M
BSP LSP
Upstream nodes

## Slide 7: Link failure protection example
Protect link P-D failure
For Destination D
  P is PLR
  N is merge point
  N advertises label N-d to P for the backup shortest-path LSP
  N-d is the shortest-path LDP LSP label at N for D
  P uses shortest-path LSP from P to N to tunnel label N-d
M
P
N
Q
S
D
N-d
Traffic flow over shortest path LSP

## Slide 8: Link failure protection fast re-routed traffic
FRR traffic paths to D when link P-D fails
P, M, N, Q, D
S, P, M, N, Q, D
M, P, M, N, Q, D
M
P
N
Q
S
D
Fast re-routed traffic
For entire network
No ‘new’ labels needed in the network
12 additional label advertisements needed
M
M-n
N-d
P-d
N-d
Q-d
D
P
M
N
Q
P-d1
M-n
N-d
D-d1
N-d
D-d1
Q-d
D-d1
D-d1

## Slide 9: Node failure protection example
Node N failure
Destination D
P is PLR
R is merge point
R advertises label R-d to P for the backup shortest-path LSP
N
P
D
Q
S
M
R-d
Traffic flow over shortest path LSP
R

## Slide 10: Node failure protection fast re-routed traffic
N
P
D
Q
S
M
Fast re-routed traffic
R
FRR traffic paths to D when node N fails
P, M, R, Q, D
S, P, M, R, Q, D
M, P, M, R, Q, D
For entire network
No ‘new’ labels needed in the network
6 additional label advertisements needed

## Slide 11: SRLG failure protection example
R
Q
D
N
M
P
S
S-d
SRLG (link P-D, link R-D ) failure
Destination D
P, R are PLRs
S is merge point
S advertises its shortest path LSP label (S-d) to P and R for failure against SRLG
Traffic flow over shortest path LSP

## Slide 12: SRLG failure protection fast re-routed traffic
R
Q
D
N
M
P
S
Fast re-routed traffic
FRR traffic paths to D when SRLG fails
P, Q, M, S, N, D
Q, P, Q, M, S, N, D
Q, R, Q, M, S, N, D
M, Q, P, Q, M, S, N, D
M, Q, R, Q, M, S, N, D

## Slide 13: Operational details
Per-nexthop protection can reduce number of BSP LSPs
What happens when a shortest-path LSP is not available for tunneling ?
  Explicit routing for BSP LSP using extensions to LDP
Protocol Extensions
  Failure Element TLV
  Tunneled FEC TLV (when label stacking not used)
  Backup Path Vector TLV

## Slide 14: Comparison with other approaches
LDP over RSVP
  Less OpEx (managing one less protocol). Simplicity.
  Less protocol state
  Multi-path on backup
LFA & Not-via
  Full coverage
  Re-uses MPLS FRR infrastructure
  No IP address management issues

## Slide 15: Future Work
Analyze applicability

## Slide 16: Questions/Comments