## Slide 1: Overlay Transport Virtualization (OTV)
Dino Farinacci
Hasmit Grover
Victor Moreno
Dhananjaya Rao

## Slide 2: Introduction
OTV is a L2/L3 Virtualization Solution for Enterprise environments
Transparent L2 extension for enterprise sites
L2 and/or L3 connectivity for site devices
Multi-site multi-point connectivity
Core transport infrastructure agnostic
Extremely simple provisioning and management

## Slide 3: Overview
MAC Routing
  Uses control plane advertisements instead of data plane learning
  Remote site MACs learnt via routing protocol
  No unknown unicast flooding through core
Inter-site data encapsulated in IP
  Routed across core to destination site
  No pre-built tunnels

## Slide 4: Overview
OTV forms an overlay network across core
Dynamically discovers member Edge Devices
EDs exchange L2 routing information
  Unicast MACs of hosts and routers in site
  Active Multicast Sources in site
  Interested Multicast Groups
OTV functionality only in edge devices
  Transparent to core and site devices
STP terminated at each site

## Slide 5
Overlay Network
L3 core
network
S1
S2
H2
H1
R1
H3
X2
S3
S4
H5
H4
R2
H6
X1
cUMRP
cUMRP
oUMRP
pUMRP
Legend:
red: switch or L2 link
green: router or L3 link
blue: L2 overlay network
R2
R1
H4
H2
H1
H5
Note: Subnets span across all sites.
VLANs span across all sites.
Each site has its own Spanning Tree.
No L2 flooding or learning on overlay.
cSTP/Snoop(1)
cSTP/Snoop(2)
Site 1
Site 2

## Slide 6: Data Forwarding
Unicast data sent to “next-hop” EDs
  Packets load-balanced across core ECMPs
Multicast uses Delivery Groups across core
  Source ED encapsulates site data in a (DS,DG)
  Core optimally replicates to interested EDs
Broadcast data sent as IP multicast
  All Edge Devices join this core multicast tree

## Slide 7: Multi-homing
OTV provides loop-free multi-homing
Authoritative Edge Device (AED) per site
  Edge Devices in the site elect AED
Only AEDs forward traffic on overlay
  Avoids loops and duplicates
Site traffic load-balanced among EDs
  Per-VLAN AED

## Slide 8: MAC Mobility
MAC moves supported by control plane
  MAC advertised with default metric
  When MAC moves, ED in new site advertises MAC with lower metric to indicate MAC move
  When original advertiser sees this, withdraws its own advertisement
  New site ED then readvertises with default metric

## Slide 9: OTV UDP Encapsulation
1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|Version| IHL |Type of Service| Total Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Identification |Flags| Fragment Offset |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Time to Live | Protocol = 17 | Header Checksum |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Source-site OTV Edge Device IP Address |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Destination-site OTV Edge Device (or multicast) Address |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Source Port = xxxx | Dest Port = 8472 |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| UDP length | UDP Checksum = 0 |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|R|R|R|R|I|R|R|R| Overlay ID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Instance ID | Reserved |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
| Frame in Ethernet or 802.1Q Format |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 10: Overlay Routing Protocol
Routing protocol for OTV control plane
  Discovers overlay members
  Forms adjacencies on overlay
  Exchanges unicast and multicast routes
IS-IS used as oUMRP
  Overlay forms a logical LAN over the core
  Edge Devices run IS-IS at L2 on overlay
  Leverages Layer-2 IS-IS extensions

## Slide 11: I-Ds
Overlay Transport Virtualization
  http://www.ietf.org/id/draft-hasmit-otv-03
IS-IS Extensions to support OTV
  http://tools.ietf.org/html/draft-drao-isis-otv-00

## Slide 12: Comments ?
Authors would like to solicit feedback and suggestions