## Slide 1: BGPSEC Potential Optimizations for AS-PATH Prepending and Transparent Route Servers.
2011.07.28 sidr-wg
sidr wg / Québec City
2011.07.28
Doug Montgomery <dougm@nist.gov>
Randy Bush <randy@psg.com>
<number>
Notes: <number>

## Slide 2
Requirements: Provide cryptographic assurance that:
  Origin AS was authorized by IP holder to announce route.
  Every AS in the AS_Path explicitly authorized the advertisement of the route to the subsequent AS in the AS_Path.
Semantics:
  Each AS’s Signature computed over Target AS for the update (forward chaining of path) and previous AS Sig (backward chaining of authorization).
  Expire Time & beaconing subject of another presentation …..
2011.07.28 sidr-wg
<number>
bgpsec-00 Level Set
AS1 Path Signature
Hash(…) Signed by Router
Key AS1.rtr-yy  Sig1
AS0 (origin) Path Signature
Hash(…) Signed by
Router Key AS0.rtr-xx  Sig0
AS1
AS2
Algo ID
Algo ID
NLRI
AS0
AS1
Sig0
Sig1
Exp Time

## Slide 3
Syntax:
  BGPSEC Path_Signatures attribute elements correspond 1-1 with AS_Path attribute elements.
  AS_Path attribute umodified, nor is Path data (ASNs) replicated in Path_Sig.
  bgpsec-00 – focus on requirements and semantics – purposefully ignore syntax optimizations until we get the first two right.
    See: draft-sriram-bgpsec-design-choices-00
2011.07.28 sidr-wg
<number>
bgpsec-00 Path_Sigs
^A0.RtrCert
Sig0
Exp Time
Algo ID
^A1.RtrCert
Sig1
……..
BGPSEC Path_Signatures Attribute
ASN 0
ASN 1
……..
BGP AS_PATH Attribute
AS_Seq

## Slide 4
From recent WG discussions:
  AS_Path Prepending – current 1-1 correspondence of elements would require repeating signatures when using Path prepending.
  Transparent Route Servers: - AS_Path does not reflect the actual sequence of AS’s that the update traversed.
Going Forward:
  Important to separate the requirement, semantics and syntax discussions of how we address these and future enhancements.
    Requirement? – ensure BGPSEC doesn’t interfere with some current/proposed use case, or enhance BGPSEC to protect use case?
  Depending upon which BGP services / capabilities / uses we are trying to preserve / protect there are numerous ways to spec solutions.
Strawman Approaches in response to recent discussions …
2011.07.28 sidr-wg
<number>
Optimizations / Enhancements

## Slide 5
Requirements:
  Support current uses of prepending without incurring expense of repeating Path_Signature elements.
  Use BGPSEC to protect prepended AS’s from modification.
Semantics:
  Prepend Count (pCNT) included as input to ASx signature noting how many times ASx appears in the actual AS_PATH.
  Normally pCNT=1.
2011.07.28 sidr-wg
<number>
Prepending Strawman
AS1 Path Signature
Hash(…) Signed by Router
Key AS1.rtr-yy  Sig1
AS0 (origin) Path Signature
Hash(…) Signed by
Router Key AS0.rtr-xx  Sig0
AS1
AS2
Algo ID
Algo ID
NLRI
AS0
AS1
Sig0
Sig1
Exp Time
pCNT
pCNT

## Slide 6: Transparent Route Servers
Use Case:
  Multi-Lateral Peering where sender does not know all the receivers.
  Router Server’s AS not included in AS_PATH so as to not contribute to the Path Length for purposes of downstream best path computation.
BGPSEC Issue:
  BGPSEC speaker can’t forward sign to other RS customers – not peering with them directly, may not even explicitly know them, defeats the transmission efficiency of RS architectures.
  Total transparency – violates the fundamental service of BGPSEC to provide a cryptographically verified sequence of route authorizations.
2011.07.28 sidr-wg
<number>

## Slide 7
Requirements:
  Support current business/use model of transparent RS’s.
  Use BGPSEC to protect / verify the complete AS_PATH (including RS AS) without impacting AS_Path_Length computations.
  Be completely transparent when sending updates to non-BGPSEC peers.
Semantics:
  RS AS fully participates in BGPSEC to/from its customer AS’s, including explicitly carrying the RS AS# in the update.
  Use previously proposed Prepend Count (pCNT=0) to indicate that an AS is operating as a transparent RS.
  BGPSEC validates complete AS_PATH, but pCNT=0 hops do not contribute to Path_Length.
  When sending to non-BGPSEC peer, RS AS# is stripped.
2011.07.28 sidr-wg
<number>
“Translucent” RS Strawman

## Slide 8
Not important now … unless we agree on the requirements/semantics:
  … if we do agree on the basic approach, then we can consider further details.
  Tradeoffs between optimization and minimizing BGPSEC changes to current BGP attributes / behaviors.
Strawman Syntax:
  Extend BGPSEC Path_Signatures Field to carry pCNT for each Sig.
    Modify Sig generation / verification procedures to address pCNT.
    Modify Path_Length computation on BGPSEC implementations to ignore pCNT=0 hops.
  Add rules to strip RS AS when sending to non-BGPSEC peer.
2011.07.28 sidr-wg
<number>
Further Details …