## Slide 1: Softwire Mesh MIB draft-cui-softwire-mesh-mib-02
Jiang Dong
Tsinghua University
2011.7
IETF 81, Quebec city

## Slide 2: Background
The WG completes RFC4925/ RFC5565 for softwire mesh
Supported by vendors
China’s Next Generation Internets: 4over6 mesh deployment in CERNET2
  A large number of PEs/client networks
  Management requirements

## Slide 3: Management requirement
Technical requirements
  Monitor the status of PEs’ mesh functions
  When broken, analyze information like BGP connectivity, NLRI-NH to find what & where is the problem
  Collect each PE’s traffic information, find the bottleneck, etc.
Manage a large number of PEs
  Produced by different vendors
  Managed by different campus networks
  Unified management is indeed necessary

## Slide 4: Relationship with Other MIBs
BGP MIB(RFC4273)
  Softwire mesh BGP peers need to negotiate tunnel type
    Need softwire mesh BGP neighbor table
IP Tunnel MIB(RFC4087)
  The IP Tunnel MIB includes softwire mesh tunnel
  Need a new tunnelIfEncapsMethod “softwireMesh”
  tunnelIfRemoteInetAddress must be set to 0.0.0.0 or ::
  tunnelIfAddressType shows address type of I-IP
  Softwire mesh tunnel is a point to multi-point tunnel
    Need softwire mesh encapsulation table

## Slide 5: Position softwire mesh MIB
swmMIB ::= {transmission xxx}
Notes: Why is under transmission

## Slide 6: Subtree of swmMIB
swmTunnelTypeTable : Supported tunnel Type
swmEncapsTable : Information about encapsulation
swmBGPNeighborTable : Information about mesh neighbors
swmMIBConformance

## Slide 7: swmTunnelTypeTable ::= {swmMIB 1}
Shows what kind of tunnel type the softwire mesh tunnel supported
  Indexed by ifIndex & swmTunnelType
  Current softwire mesh tunnel supports IP-IP, GRE, L2TPv3 (section 4 of RFC5512)

## Slide 8: swmEncapsTable ::= {swmMIB 2}
A encapsulation table of the softwire mesh tunnel, including IPv4-over-IPv6 and IPv6-over-IPv4
  Indexed by ifIndex & swmEncapsEIPDst & swmEncapsEIPMask
  Address type is decided by tunnelIfAddressType in tunnelIfTable
Objects
  Destination (E-IP destination address + mask)
  Encapsulation header (I-IP destination address)

## Slide 9: swmBGPNeighborInfo ::= {swmMIB 3}
BGP neighbor information of the softwire mesh tunnel
  Indexed by ifIndex & swmBGPNeighborAddress
Objects
  BGP neighbor address
  negotiated tunnel type with each neighbor

## Slide 10: Discussion
Collaboration welcomed. Please jump in if you’re interested.
Suggestions? Anything we miss?