## Slide 1
Softwire Mesh Multicast
draft-xu-softwire-mesh-multicast-02
Mingwei Xu, Yong Cui, Shu Yang
Tsinghua University
Chris Metz, Greg Shephard
Cisco
IETF81 Meeting, Quebec
July 2011
Notes: <number>
照抄上个ppt
<number>

## Slide 2: Softwire Deployment in CERNET2
<number>
Softwire gateways will be deployed in 100 campus networks in September, 2011
Next step: Implement multicast modules in softwire gateways
Notes: <number>
本页是基本需求
迁移：用户位置，通信可中断，但识别同一个身份
漫游：位置移动，通信不断
<number>

## Slide 3: Changes from Version 01
Separated description for SSM and ASM
Stateless source address mapping instead of RPF vector in 4over6 scenario
Stateless source address mapping instead of AFBR signaling in 6over4 scenario
Notes: <number>

## Slide 4: Scenario of Softwire Mesh Multicast
(*,G) or (S,G)
(S’,G’)
(*,G) or (S,G)
To simplify the process, stateless one-to-one source address and group address mapping is applied
Notes: <number>
根据陈文龙师兄以前的建议对上个ppt中的图进行了修改

## Slide 5: Four Detailed Scenarios
E-IP supports SSM, I-IP supports SSM
  S should be embedded in S’
  S’ must lead the message to the upstream AFBR
E-IP supports SSM, I-IP supports ASM
  The same as the first scenario
E-IP supports ASM, I-IP supports SSM
  * should be embedded in S’
  S’ must lead the message to the corresponding upstream AFBR (RP’)
E-IP supports ASM, I-IP supports ASM
  The same as the third scenario
Notes: <number>

## Slide 6: Source Address Mapping (4over6)
prefix: a “well-known“ prefix or a ISP-defined prefix
  An existing “well-known" prefix is 64:ff9b, which is defined in RFC6052
v4: the IPv4 address of the E-IP interface of upstream AFBR
u: must be set to zero
suffix: reserved for future extensions and should be set to zero
source address: original S or *
prefix | v4 | u | suffix | source address
0
32
72
96
64
128
Notes: <number>
refer to RFC6052

## Slide 7: Source Address Mapping (6over4)
prefix: a “well-known“ prefix or a ISP-defined prefix
  An existing “well-known" prefix is 64:ff9b, which is defined in RFC6052
v4: the mapped I-IPv4 address of S or *
prefix | v4
0
96
128
Notes: <number>

## Slide 8: Group Address Mapping
draft-boucadair-behave-64-multicast-address-format-02
scop & flag: Defined in [RFC4291].
64IX: When "M-bit" is set to 1, it indicates that an multicast IPv4 address is embedded in the “v4 address” field. All the remaining bits MUST be set to 0.
sub-group-id: The default value is all zeros.
v4 address: include an IPv4 multicast address when the M-bit is set to 1
11111111 | 0011 | scop | 00….00 | 64IX | sub-group-id | v4 address
0
20
36
96
32
128
8
12
11111111 | flags | scop | 64IX | sub-group-id | v4 address
16
ASM mode
SSM mode
M | r | r | r
64IX:
Notes: <number>
refer to draft-boucadair-behave-64-multicast-address-format-02

## Slide 9: Next Step
WG document adoption?