## Slide 1: Multicast Extensions to DS-Lite Technique in Broadband Deployments draft-qin-softwire-dslite-multicast-04
Wang, Q., Qin, J., Boucadair, M., Jacquenet, C., and Y. Lee

## Slide 2: Context & Use Cases
Context
  Deliver multicast-based service offerings to DS-Lite serviced customers in ASM and SSM modes
Use Cases
  IPv4 receiver accessing IPv4-framed multicast content
  Dual-Stack receiver accessing IPv4-framed multicast content

## Slide 3: Foundations
Address Building
  Use [I-D.boucadair-behave-64-multicast-address-format] to build multicast IPv4-embedded IPv6 addresses
  Use [RFC6052] to build unicast IPv4-embedded IPv6 addresses representing IPv4 sources in the IPv6 realm
The underlying network delivers encapsulated packets in standard multicast fashion
  Bandwidth optimization is ensured
All involved interworking functions are stateless

## Slide 4
IPv4 Source
IPv4 Receiver
mAFTR
mB4
IGMP
MLD
QR
MLD Querier
IPv6 PIM
IPv4 PIM
IPv4 Flows
IPv4-in-IPv6 Flows
Stateless IPv4-IPv6 PIM Interworking Function
Stateless IGMP-MLD Interworking Function
Stateless encapsulation
&
IPv4 -> IPv6 header mapping
of multicast flows
Overall procedures with involved interworking functions:
Need to provision the mB4 with mPREFIX64 and uPREFIX64
IPv4 Realm
IPv6 Realm
IPv4 Flows
DR
R
S
IPv4 Realm
Stateless de-encapsulation of multicast flows
CPE

## Slide 5: ASM/SSM Discussion
Shared tree computation (ASM)
  Transparent in the IPv4 side
  In the IPv6 side
    For the sake of simplicity, it is RECOMMENDED to configure an mAFTR as the RP for IPv4-embedded IPv6 multicast groups
    If some other IPv6 multicast router wants to become the RP of the IPv4-embedded IPv6 multicast groups, it may require an mAFTR to emulate the PIM Source Register procedure on behalf of IPv4-embedded IPv6 sources with the RP
      The PIM Source Register procedure in the IPv4 domain is not altered
  Switching to a SPT tree computation is natively supported where the mAFTR would become the source of the IPv6 MDT and perform the translation
SSM Mode is supported

## Slide 6: Difference to -03
“Fall-Back” mode removed
  There is another draft discussing this mode
    I-D-sarikaya-softwire-dslitemulticast
  Which relies on the original design of DS-Lite (i.e., Unicast-based tunnel) to deliver multicast traffic
  The efficiency of multicast traffic forwarding between B4 and AFTR will be lost in this mode

## Slide 7: Next Step
Adopt this I-D as a Working Group document