## Slide 1: Multicast Support for Dual Stack Lite
Behcet Sarikaya
draft-sarikaya-softwire-dslitemulticast-00.txt

## Slide 2: DS-Lite Multicast
DS-Lite B4 MUST support IGMP Proxy
DS-Lite AFTR MUST support IGMP Querier
ASM/SSM transparently supported
For SSM, IGMPv3 must be supported
IPv4
Internet
AFTR - CGN
NAT44
(Private->Public)
IPv6
Internet
IPv4
IPv6
B4 - CPE
(dual-stack)
Home Network
IPv6 Network
IPv6
IPv4
Private IPv4 Address
4-in-6 tunnel
IGMP Proxy
IGMP Querier

## Slide 3: DS-Lite Multicast Operation
B4 establishes a tunnel interface with AFTR
IGMP messages and v4 multicast data are carried in v4 in v6 tunnel between B4 and AFTR
B4 sends aggregated IGMP report messages to AFTR
B4 receives v4 multicast data, decapsulates it and then delivers it to the hosts
Due to the shared link no duplication is needed
AFTR acts as the default multicast querier for all B4s
AFTR receives v4 multicast data, first replicates and then forwards in IPv4-in-IPv6 tunnel to B4s
PROS: Encapsulation based no translation
PROS: Does not require native multicast in access

## Slide 4: Layer 2 Support
Assumption: DS-Lite network supports IPv4 multicast in Layer 2
Switches maintain a list of multicast routers and the ports using multicast router discovery protocol (RFC 4286)
IGMP join/leave messages add/remove filter entries
Multicast data packets are forwarded downstream based on the filter entries
IPv4 snooping switches IPv6 protocol field values in IPv4-in-IPv6 tunnel

## Slide 5: Next Steps
WG draft?