## Slide 1: Multicast Support for 6rd
Behcet Sarikaya
draft-sarikaya-softwire-6rdmulticast-01.txt

## Slide 2: 6rd Multicast
6rd CPE MUST support MLD Proxy
6rd BR MUST support MLD Querier
ASM/SSM transparently supported
For SSM MLDv2 must be supported
IPv4 Network
IPv6 Network
6rd BR
IPv6
IPv4
CE
6-in-4 tunnel
MLD Proxy
MLD Querier

## Slide 3: 6rd Multicast Operation
6rd customer edge device (CE) is MLD Proxy
6rd CE establishes tunnel interface with 6rd BR
MLD messages and v6 multicast data are carried in v6 in v4 tunnel between CE and BR
The protocol is analogous to DS-Lite multicast but instead of IGMP, MLD is supported
PROS: Encapsulation based no translation
PROS: Does not require native multicast in access

## Slide 4: Layer 2 Support
Assumption: 6rd network supports IPv6 multicast in Layer 2
Switches maintain a list of multicast routers and the ports using multicast router discovery protocol (RFC 4286)
MLD join/leave messages add/remove filter entries
Multicast data packets are forwarded downstream based on the filter entries
IPv6 snooping switches IPv4 protocol field values in IPv6-in-IPv4 tunnel

## Slide 5: Next steps
WG draft?