## Slide 1: 4rd @ IETF 81
draft-murakami-softwire-4rd-00
(Satoru Matsushima / Tetsuya Murakami / Ole Trøan)
DS-lite
6rd
A+P
4rd

## Slide 2: Draft history
draft-despres-softwire-4rd-00 (2010-10-18)
draft-despres-intarea-4rd-00 (2011-03-07)
draft-despres-intarea-4rd-01 (2011-03-14)
draft-murakami-softwire-4rd-00 (2011-07-04)
Motivation draft: draft-operators-softwire-stateless-4v6-motivation-02
Applicability statement: draft-sun-intarea-4rd-applicability-01
DHCPv6 option: draft-mrugalski-dhc-dhcpv6-4rd-00

## Slide 3: 4rd in One Slide
IPv4 + IPv6
IPv4 + IPv6
IPv4 + IPv6
  Native dual-stack IP service to the Subscriber
Simple, stateless, automatic IPv4-in-IPv6 encap and decap functions
IPv4 traffic automatically follows IPv6 Routing
  BRs placed at IPv4 edge, addressed via anycast for load-balancing and resiliency
Defined in draft-murakami-softwire-4rd
IPv6
CE
4rd Border Relays
Dual Stack Core
4rd
4rd
4rd
4rd
“One line” global config for IPv6 Gateway
Subscriber IPv4 address or prefix derived from IPv6 address

## Slide 4: Comparison
4rd aka Stateless DS-lite | Stateful DS-lite
NBMA link | Hub and spoke tunnel
Algorithmic mapping between payload addresses and tunnel endpoint addresses | Configured tunnel with tunnel endpoints configured on AFTRs
Implicitly provisions IPv4 address, prefix or shared IPv4 address | No address provisioning
Scales by traffic | Scales by number of customers
Resiliency achieved by native routing, anycast and multiple BRs | Resiliency achieved by AFTRs never crashing  (Proprietary HA solutions, probing…)
NAT44 on CPE (port restricted) | NAT44 on AFTR
Fixed port set allocated on customer provisioning. (A source port can be bound to many destinations) | Port set limited only by total amount of ports on AFTR
Increase of port space can be done with additional mapping rules or renumbering | Just add more IPv4 addresses on AFTR
4rd CE apps use private address | Private Address

## Slide 5: 4RD : Stateless Address Mapping
Domain IPv4
prefix
EA-bits
48bit (IPv4 + Port)
Domain IPv6
prefix
EA-bits
Suffix
Interface ID
Port
Head
Port Set ID
32bit
128bit
Port
0
0
0
1
0
0
1
0
1
1
Provisioning based on elements that are:
Well known
Derived from IPv6 provisioning
Provisioned via DHCPv6
Embedded in address

## Slide 6: IPv4 Address Sharing – Port-set ID deriving
6
IPv4 Internet
4rd BR
CE IPv6 Prefix:
2001:db8:cdab::/48
CE IPv6 Prefix:
2001:db8:cdef::/48
CE IPv6 Prefix:
2001:db8:cda1::/48
4rd
CE1
4rd
CE2
4rd
CE3
Domain IPv6 Prefix:
2001:db8::/32
If there is a remainder of EA bits, this part will be treated as Port-set ID.
Shared IPv4 Address:
192.0.2.205
Port-set ID: 0xab
Shared IPv4 Address:
192.0.2.205
Port-set ID: 0xef
Shared IPv4 Address:
192.0.2.205
Port-set ID: 0xa1
Domain IPv6 prefix
EA bits
CE IPv6 prefix (max 64bits)
Domain 4rd prefix
IPv4 shared address
(32 bits)
Port-set ID
(max 15 bits)
CE 4rd prefix (33~47 bits)
ISP’s IPv6 Network
The Port-set ID is 8 bits, so 256 customers can share one IPv4 address of 192.0.2.205.
EA bits

## Slide 7: Port allocation algorithms:
Algorithm | Description | 
Port sets with heads | 0001 KKKK KKPP PPPP - 64 ports 001K KKKK KPPP PPPP - 128 ports 01KK KKKK PPPP PPPP - 256 ports 1KKK KKKP PPPP PPPP - 512 ports Works up to a sharing ratio of 4096 (16 ports per customer) | Consecutive ports
Prefix based | E.g: a /6 gives 1024 ports. | Consecutive
Modulo | P=j*N + K + 1024, for of j=0, 1, ..., (65536-1024-N)/N K=((P-1024) % N) (P – Ports, N – Sharing ratio, K – port set ID) e.g: N=64, K=1 gives P={1025 1089 1153 1217 1281 1345…} | Scattered

## Slide 8: Next:
WG adoption