## Slide 1: 4via6 Stateless Translation draft-murakami-softwire-4v6-translation-00.txt IETF 81-Quebec, July 2011
T. Murakami(Ed.), G. Chen, H. Deng, W. Dec and S. Matsushima

## Slide 2: Overview
A group of operators worked together on draft-operators-softwire-stateless-4v6-motivation-02
  France Telecom, Softbank Telecom, Comcast, Deutsche Telekom, Portugal Telecom and China Mobile
4via6 stateless manner could work on both translation and tunneling mode
  Translation solution, draft-murakami-softwire-4v6-translation-00
  Tunneling solution, draft-murakami-softwire-4rd-00
In order to clearly explain why 4via6 stateless translation solution is needed
  draft-dec-stateless-4v6-02 has been proposed

## Slide 3: 4via6 Stateless Translation
It uses IPv6/IPv4 protocol translation in order to transport IPv4 packets across IPv6-only network
It’s suitable to be deployed in mobile environments in which CPEs with wireless modem use 3GPP access as uplink
3GPP core network
Internet
CPE
UEs
BR
Notes: <number>

## Slide 4: Behaviors of 4via6 Stateless Translation
4via6 CE
  Generate an IPv4 address or an shared IPv4 address and port-set
  Translate an IPv4 packet from/to an IPv6 packet
Mapping rule
  4via6 CE—>BR
    Source address: 4rd mapping rule
    Destination address: RFC6052
  4via6 CE —> 4via6 CE
    Source and destination address: 4rd mapping rule
NAT44
  The behavior is conforming to best current practice
  Translate the port number into the port-set generated in a given 4via6 CE
4via6 BR
  Stateless translation at edge of 4via6 domain
Notes: <number>

## Slide 5: 4via6 translation is suitable to the mobile network
The translation solution in a mobile provider context requires less system changes (No impacts on core network elements)
4via6 translated traffic can be handled using existing native IPv6 functionality defined by the core 3GPP specifications. It keeps the operator's service model intact.
This form of deployment has no noticeable impact on the users

## Slide 6
<number>
Application | Status | Note
Mail (POP, IMAP, SMTP) | OK | 
Skype | OK | 
ICMP Echo Request/Reply | OK | 
OWA | OK | 
iTunes | OK | 
Web Access (GoogleMap) | OK | 
Web Access (Youtube) | OK | 
Web Access (Other sites) | OK | 
PPTP | NG | PPTP can be passed if using ALG.
IPSec/UDP | OK | UDP encapsulation is required.
Twitter | OK | 
EverNote | OK | 
DropBox | OK | 
Google Earth | OK | 
Bittorrent | OK | 
ssh/telnet/ftp | OK | 
Confirmed Application based on testing

## Slide 7: Proposal
Accept 4via6 stateless translation as working group draft
Many Thanks!