## Slide 1: Public IPv4 over Access IPv6 network
draft-cui-softwire-host-4over6-06
draft-cui-softwire-dhcp-over-tunnel-01
Y. Cui, J. Wu, P. Wu Tsinghua Univ.
C. Metz Cisco Systems
O. Vautrin Juniper Networks
Y. Lee Comcast
T. Lemon Nominum

## Slide 2: Public 4over6: basic idea
B4
AFTR
(NAT)
Dual-stack lite:
v4-in-v6 tunnel
SERVER
AFTR
(no NAT)
v4-in-v6 tunnel
B4
(NAT)
AFTR
(no NAT)
v4-in-v6 tunnel
Public 4over6:
host
host
host
4over6
initiator
4over6
concentrator
When allocating public address to B4…

## Slide 3: Change logs
-00 version in July 2010
Both stateful and stateless solution in -01 -02 version
WG asks us to accomplish the stateful solution first(-03, -04 version)
changes since -04 version
  Split DCHPv4 over IPv6 to a dedicated draft
  Add use cases analysis
  Remove the Non-NAT CPE case
  Mapping maintenance method changes for HA/security concern

## Slide 4: Documents
DHCPv4 over IPv6 document
  --draft-cui-softwire-dhcp-over-tunnel-01
  IPv4 addr allocation from concentrator to initiators
    Server-side DHCP Encapsulation
Public 4over6 mechanism document
  --draft-cui-softwire-host-4over6-06
  Motivation and use cases
  Encapsulation and Decapsulation mechanism
    Concentrator discovery for initiator
    Address mapping maintenance on concentrator

## Slide 5: DHCPv4 over IPv6
Apply DHCP to client=tunnel=server environment
  All DHCPv4 packet interaction over IPv6
Main issue
  IPv6 Forwarding header of DHCP replies on server
    Need correct IPv6 destination address
2000::1001
2000::1
DHCP server
2000::2001
DHCP client
DHCP reply
(offer/ack/nak)
DHCPv4 packets
IPv6
dest IPv6 addr?

## Slide 6: DHCPv4 over IPv6 solutions
Solution1: server keeps temporary (IPv6 address, DHCP session ID) mapping
  Could be DHCP transaction-id, MAC address
Solution 2: leveraging Relay Agent option(or new option?)
  Client includes the TI IPv6 address in Option 82
2000::1001
2000::1
2000::2001
Encap dest addr?
Store (ID, TI IPv6 addr) mapping
when receving DHCPv4
Lookup IPv6 addr using ID
when sending DHCPv4
Solution 1
Solution 2
Find IPv6 addr in option 82
when sending DHCPv4
Use option 82 with
TI IPv6 addr

## Slide 7: Encapsulation and decapsulation
Encapsulation destination address
Initiator: concentrator IPv6 address
  Provided by DHCPv6 option
    Same as [draft-ietf-softwire-ds-lite-tunnel-option-10]
Concentrator: correct initiator IPv6 address
  Maintain mapping of (allocated IPv4 address, initiator IPv6 address)
    Lookup IPv6 encap destination address using IPv4 destination address

## Slide 8: DHCP driven IPv4-IPv6 Mapping maintenance
The mapping is maintained along with DHCPv4 allocation
Concentrator as DHCP Relay or Server
Install/renew the address mapping when relay/send out DHCPv4 Ack
Used for destination address lookup when encap
IPv4
IPv6 Edge Network
Local IPv4
Network
TI
TC
2000::1001
59.66.1.1
DHCPv4 request
DHCPv4 ack
Relay
Server
DHCPv4 server
Client

## Slide 9: Prototype Implementation
Concentrator and CPE initiator: Linux
Host initiator: Linux, WIN XP and WIN 7
Release before next IETF, demo available now
Test deployment: CERNET, Tsinghua & BUPT Univ., …
CERNET2 v6
IETF v6
CERNET v4
Public 4over6
4over6 TC
4over6 TI

## Slide 10: Document Status
Presented in IETF78, 79, 80
Received many comments from the meetings/ mailing list and revise accordingly.
Working Group milestone
  Jul 2011 Adopt DS-Lite without NAT document as a WG document
  Jul 2011 Adopt DHCPv4 over tunnel document as a WG document
Request for adoption as a WG document