## Slide 1: ITU-T Q13/15 Updates
TICTOC / IETF-81
Stefano RUffini, Ericsson; Q13/15 Associate Rapporteur

## Slide 2: Introduction
Q13/15 held an Interim meeting in May 2011 hosted by ATIS (Indianapolis)
Two main topics of interest for TICTOC:
  Packet timing performance aspects for frequency (G.826x series)
    PDV metrics
    Network limits
    Packet clock specification
  Time Sync in packet networks (G.827x series)
    Network Limits
    Clocks
    Architecture and Telecom Profiles

## Slide 3: Current Doc. Structure

## Slide 4: Frequency SYnc Updates
G.8260
  Appendix on PDV Metrics updated at last Q13/15 Interim meeting
  Several agreements reached on the PDV metrics:
    Metrics to be used for normative requirements should have a fixed bandwidth and should have packet pre-selection; under discussion the use of MAFE (packet selection details under discussion)
    Delay jumps and start up are out of scope for now
  Confirmed plans to consent the Amendment in December 2011
Ongoing discussions on the packet clock (G.8263);
  Draft G.8263 has been updated at last Q13/15 Interim meeting
  Focus on mobile application; Packet clock external to the Base Station for now.
  PDV Tolerance mask aligned with the G.8260 normative metrics
  Noise Transfer as a combination of the “target requirements” and of the PDV tolerance characteristics
  The time constant is among aspects under discussion
  Confirmed plans to consent the recommendation in December 2011
Ongoing discussions on the network limits (G.8261.1)
  Draft G.8261.1 has been updated at last Q13/15 Interim meeting
  Focus on mobile application
  Network Limits based on the G.8260 normative metric
  The packet selection details are among aspects under discussion
  Confirmed plans to consent the recommendation in December 2011

## Slide 5: PDV MEtrics for network limits
Pre-Processing
Fixed Bandwidth
Exception: MAFE, unless calculated in a single value corresponding to the “fixed bandwidth”

## Slide 6: Time Sync Updates
G.8271 (Time sync requirements)
  Draft G.8271 has been updated at last Q13/15 Interim meeting
  Improved section on the time sync error sources and simulation model
  Information on GNSS-based solutions ha sbeen added
  Class of time sync requirement in the 500 ns -1 microsecond range has been added
  Confirmed plans to consent the recommendation in December 2011
Time Sync Architecture and PTP Profile (G.8275 and G.8275.1)
  Ongoing discussions
  Confirmed priority for a reference network with only BCs; TC still under discussion
  Recommendations planned to be consented in 2012
Time Sync Clocks (G.8272, G.8273.x)
  Ongoing discussions on the PRTC and Telecom BC characteristics
  No draft updated at last meeting