## Slide 1: Checksum Trailer in Timing Protocols draft-mizrahi-tictoc-checksum-trailer-00 http://tools.ietf.org/html/draft-mizrahi-tictoc-checksum-trailer-00
Tal Mizrahi
Marvell
IETF Meeting 81, July 2011

## Slide 2: Background
Timing protocols transported over UDP:
  IEEE 1588.
  NTP.
  OWAMP/TWAMP.
UDP over IPv4 (RFC 768):
  Checksum can be 0, causing receiver to ignore checksum.
UDP over IPv6 (RFC 2460):
  Checksum is mandatory.

## Slide 3: Intermediate Nodes
IEEE 1588 Transparent Clock (TC):
Internal intermediate node (NTP – RFC 5905 / OWAMP – RFC 4656 / TWAMP – RFC 5357):
Intermediate nodes must re-computed the UDP checksum or incrementally update it (RFC 1624).

## Slide 4: Overview
PTP over IPv6 (Annex E of IEEE 1588):
  2 bytes added to the end of the PTP payload.
  Can be used by an intermediate node for incremental checksum update.
Current draft:
  Define Checksum Trailer for NTP and for OWAMP/TWAMP.
  Allow intermediate node to perform incremental checksum update.

## Slide 5: Checksum Trailer
+--------------------------------+
| IPv4 / IPv6 Header |
.................+--------------------------------+
^ | UDP Header |
| .........+--------------------------------+
| ^ | |
UDP | | NTP / PTP / OWAMP / TWAMP |
Length UDP | packet |
| Payload +--------------------------------+
| | |UDP Checksum Trailer (2 octets) |
v v +--------------------------------+

## Slide 6: NTP Checksum Trailer
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Field Type | Length = 16 octets |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
| Padding |
| |
| +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| | Checksum Trailer |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Use NTP Extension Field.
Need to define Field Type for Checksum Trailer.

## Slide 7: OWAMP/TWAMP Checksum Trailer
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sequence Number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Timestamp |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Error Estimate | |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ |
| |
. Packet Padding .
. .
| +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| | Checksum Trailer |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Use the OWAMP padding field.
Padding length is announced in the Request-Session message.

## Slide 8: Interoperability with Existing Implementations
OWAMP padding  no new requirements from receiver.
NTP extension field – open issue regarding existence of MAC.
NTP, OWAMP/TWAMP:
  The intermediate node and the originator of the packet are managed by the same entity.
  Either both use the Checksum Trailer, or both do not use it.

## Slide 9: Next Steps
July 2011 – draft 00.
Receive feedbacks from WG.