## Slide 1: TRILL ESADI draft-hu-trill-rbridge-esadi-00
Hongjun Zhai (ZTE)
Fangwei hu (ZTE)
Radia Perlman (Intel Labs)
Donald Eastlake 3rd (Huawei)
July 2011
<number>
TRILL ESADI
Notes: <number>
November 2010
TRILL OAM & BFD

## Slide 2: Motivate
ESADI( End System Address Distribution Information): a optional VLAN scoped way that RBridges can announce and learn end station addresses rapidly and securely
Advantage:
  Security advantages: announces end stations with an authenticated enrollment , ESADI protocol supports cryptographic authentication
  Fast update advantages: provides a fast update of end station MAC addresses
July 2011
TRILL ESADI
<number>

## Slide 3: Motivate
Why do we need a new ESADI draft?
  Move the MAC and parameters from ISIS PDU to ESADI frame
    In the Basic TRILL RFC(RFC6325), TRILL parameters and MAC addresses are carried by TRILL IS-IS PDU. The ESADI MAC address flooding has effect on TRILL control plane, which reduces the TRILL robust and reliability
    In the new draft, TRILL MAC addresses and parameters are carried in ESADI frames rather than in the core TRILL IS-IS protocol, the ESADI frame is encapsulated as multicast TRILL data traffic. By this design, ESADI is a virtual logical topology (for each VLAN ) overlay in the TRILL topology.
  Rich and complement the ESADI protocol
    Design DRB election state machine , ESADI sub-TLV , etc.
July 2011
TRILL ESADI
<number>

## Slide 4: Overview
ESADI RBridge:
    The RBridge is appointed VLAN-x forwarder and participants in ESADI protocol is called an ESADI RBridge
Transit RBridge:
    Forward ESADI frame as multicast TRILL data frame
All the ESADI RBridges appear to be directly connected by a shared virtual link for that VLAN
No “routing” computation or decisions ever have to be made by ESADI
No Hello frame between ESADI RBridges
July 2011
TRILL ESADI
<number>

## Slide 5: TRILL ESADI Structure
July 2011
TRILL ESADI
<number>
ESADI frames encapsulation in transit on Ethernet links is similar with TRILL encapsulation with an outer Ethernet header
ESADI frame has an inner Ethernet header with the Inner.MacDA of “All- ESADI-RBridges” and the “L2-IS-IS” Ethertype followed by the ESADI payload.

## Slide 6: ESADI DRB Election
July 2011
TRILL ESADI
<number>
E1: Operationally up
E2: Finding first neighbor
E3: Holding Timer expired
E4: Receiving higher priority PDU
E5: Losing last neighbor
E6: Operationally down
Down: Virtual state
Initial: ESADI instance is up but does not know of any ESADI neighbors
Not-DRB: ESADI instance has found at least one valid ESADI neighbor and is not DRB yet
DRB: ESADI instance multicasts the ESADI CSNP PDUs periodically, and responds to ESADI-PSNP PDUs with ESADI-LSPs.
TRILL ESADI state diagram

## Slide 7: ESADI LSP contents
ESADI participation data sub-TLV
  MUST be included in LSP fragment zero
July 2011
TRILL ESADI
<number>

## Slide 8: ESADI LSP contents
ESADI MAC Address sub-TLV
  TRILL ESADI LSP PDUs consists of one or more MAC Reachability (MAC-RI) TLVs
  specified in [RFC6165].
  These sub-TLV contain one or more unicast MAC addresses of end stations
July 2011
TRILL ESADI
<number>

## Slide 9: Summary
What do we do in the new ESADI draft (difference with RFC6325 )?
  Move MAC addresses and parameters in TRILL IS-IS protocol to ESADI frames
  Design DRB election state machine
  design ESADI neighbor list
  design PDU processing , optimize self-originated LSP to be sent in unicast in stead of multicast in some situation to reduce multicast storm.
  Specific ESADI Participation Data TLV to announce ESADI capability for RBridges
July 2011
TRILL ESADI
<number>

## Slide 10: END
March 2011
<number>
TRILL OAM
Hongjun Zhai (ZTE)
Fangwei hu (ZTE)
Radia Perlman (Intel Labs)
Donald Eastlake 3rd (Huawei)
Notes: <number>
November 2010
TRILL OAM & BFD