## Slide 1: Fine-Grained VLAN Labeling draft-eastlake-trill-rbridge-fine-labeling-01.txt
Radia Perlman
Intel Labs
radiaperlman@gmail.com
July 2011
<number>
IETF TRILL WG
Notes: <number>
July 2011

## Slide 2: Goals
More VLANs
Work with existing silicon
Allow existing RBridges to work in the core
Make sure misconfigurations (having old RBridges on the edge) don’t do anything bad
Opportunistic opportunity: 2nd priority field
July 2011
<number>
IETF TRILL WG

## Slide 3: Basic Idea
Use two VLANs (in the inner packet), to encode 24 bits of VLAN (16 million)
July 2011
<number>
IETF TRILL WG

## Slide 4: Double VLAN tag
outer Ethernet hdr
unchanged
TRILL header
unchanged
dest MAC
source MAC
VLAN INFO
payload
Link Trailer
this is what changes
for fine-grained labeling
Old: single VLAN tag
Fine-grained: two consecutive
VLAN tags (both “C”)
July 2011
<number>
IETF TRILL WG

## Slide 5: Notation
ST=“Single Tag” RBridge, i.e., not fine-grained labeling aware
DT=“Double Tag” RBridge, i.e., fine-grained labeling aware
(X.Y) = Fine-grained label with first 12 bits=X, and 2nd 12 bits=Y
July 2011
<number>
IETF TRILL WG

## Slide 6: Reporting DT-capability
DT RBridges will report their DT-capability in LSPs
So therefore DT RBridges will know which RBridges are ST, and which are DT
July 2011
<number>
IETF TRILL WG

## Slide 7: Reporting Attached fine-grained labels
New sub-TLV in LSP for appointed forwarder to report attachment to a range of 24-bit labels
Will be ignored by ST RBridges
July 2011
<number>
IETF TRILL WG

## Slide 8: Some issues with mixing ST and DT RBridges
If ST RBridge in core, make sure it doesn’t falsely filter multidestination (letting extra traffic through is OK, but blocking traffic because confusion with double tag not OK)
If core ST RBridge exists, then DT R2 attached to X.Y must report attachment to ST VLAN “X”
To allow some ST edge RBridges, we will allow some VLANs (say first k) to be announced with a single tag, whether ingressed by DT or ST
July 2011
<number>
IETF TRILL WG

## Slide 9: Illegal configuration
Illegal if ALL of the following are true
  Single tag VLAN “X” exists
  Double tag VLAN “X.Y” exists
  There is a ST RBridge on the edge reporting it is connected to X
Detected through LSPs
Mediated by having DT RBridge that is appointed forwarder for DT VLAN X.Y refrain from ingressing or egressing VLAN X.Y, and complaining
July 2011
<number>
IETF TRILL WG

## Slide 10: ST in core
The only time core RBridges look at VLAN tag is for filtering multidestination frames
It’s OK for filtering not to be perfect (i.e., only filter on 12 of the 24 VLAN bits – it just wastes a bit of bandwidth, and filtering is a SHOULD anyway, not a MUST)
But must not falsely filter
July 2011
<number>
IETF TRILL WG

## Slide 11: Avoiding false filtering with ST R1 in core
To make sure that R1 doesn’t falsely filter (X.Y), all edge RBridges attached to any fine-grained label with the first 12 bits=X must report connectivity to ST VLAN “X” in addition to DT VLAN (X.Y)
July 2011
<number>
IETF TRILL WG

## Slide 12: Unicast
Basically no change, except for priority
Given there are two VLAN tags, there’s two priority fields
Transit RBridges use the priority in the first VLAN tag
July 2011
<number>
IETF TRILL WG

## Slide 13: Possible Variant
There might be reasons for R1 to send a multidestination frame as several unicasts instead
  there might be a very small number of edge RBridges that need to see the frame (e.g., a VLAN that only exists at a few places)
  As an alternative instead of disabling connectivity to X.Y, when illegal configuration
It is optional for ingress to send, but mandatory for egress to receive a multidestination frame as a directed unicast
July 2011
<number>
IETF TRILL WG