## Slide 1: Pseudonode Nickname draft-hu-trill-pseudonode-nickname-00
Hongjun Zhai (ZTE)
Fangwei Hu (ZTE)
Radia Perlman (Intel Labs)
Donald Eastlake 3rd (Huawei)
July 2011
<number>
Pseudonode Nickname
Notes: <number>
November 2010
TRILL OAM & BFD

## Slide 2: Contents
Problem Statement
  Traffic failure caused by AF change
Pseudonode Nickname
Control Plane of Pseudonode Nickname
Data Plane of Pseudonode Nickname
TLV Extension for Pseudonone Nickname
July 2011
Pseudonode Nickname
<number>

## Slide 3: Problem Statement
Only AF(Appointed Forwarder) can ingress/egress native frames into or from TRILL network on a multi-access link
VLAN-x AF changes for some reasons:
  DRB changed, and the new DRB maybe designate another RBridge as VLAN-x AF in the link
  AF down or overloaded, DRB designates another RBridge as VLAN-x AF
July 2011
<number>
Pseudonode Nickname

## Slide 4: Problem Statement
Issues caused by VLAN-x AF changing:
  End station can not perceive the AF change
  MAC entries in remote RBridge’s cache can not be updated by self-learning in time
  Remote traffic to local end station will be destined to the stale VLAN-x AF, and be discarded
  ESADI can alleviate the issues, but it is only an optional protocol, not running on all ingress/egress RBridges
  It is even worse for the Swap Nickname Field approach in multi-level TRILL
July 2011
<number>
Pseudonode Nickname

## Slide 5: Problem Statement
Issues caused by VLAN-x AF changing(examples):
July 2011
<number>
Pseudonode Nickname
RB3
RB2
RB1
TRILL Campus
H2
H1
RB4
H3
E1
E2
RB2
RBx
RBy
In the RB3’s forwarding table, egress is an RBridge, not a link or a group of RBridges, which causes the issue
D_MAC Egress
H1 RB1
… …

## Slide 6: Contents
Problem Statement
  Traffic fails caused by AF change
Pseudonode Nickname
Control Plane of Pseudonode Nickname
Data Plane of Pseudonode Nickname
TLV Extension for Pseudonone Nickname
July 2011
Pseudonode Nickname
<number>

## Slide 7: Pseudonode Nickname
Issues is solved by pseudonode nickname:
July 2011
<number>
Pseudonode Nickname
RB3
RB2
RB1
H2
H1
RB4
H3
E1
E2
RB2
RBx
RBy
PseNick1
[10]
[10]
[15]
[xx]: cost of link
In the RB3’s forwarding table, egress is the pseudonode nickname of E2 link, not an RBridge, so the issue is solved
D_MAC Egress
H1 PseNick1
… …
TRILL Campus

## Slide 8: Pseudonode Nickname
Pseudonode nickname is used to identify a link or a group of Rbridges
It is assigned by DRB on the link:
  If there is not a pseudonode nickname on a link, the DRB will contend for one (just as an RBridge nickname) and announce it in its hellos
  Else, the DRB should reuse the existing pseudonode nickname on this link
July 2011
<number>
Pseudonode Nickname

## Slide 9: Contents
Problem Statement
  Traffic fails caused by AF change
Pseudonode Nickname
Control Plane of Pseudonode Nickname
Data Plane of Pseudonode Nickname
TLV Extension for Pseudonone Nickname
July 2011
Pseudonode Nickname
<number>

## Slide 10: Control Plane of Pseudonode Nickname
Pseudonode nickname function
  Each RBridge on the link announces its pseudonode nickname capability in its TRILL Hellos
  Only if DRB confirms that all the adjacencies in Report state support and enable this capability, this function can be enabled on the link
July 2011
<number>
Pseudonode Nickname

## Slide 11: Control Plane of Pseudonode Nickname
  Pseudonode nickname in Hellos:
  Each RBridge announces the pseudonode nickname used on this link if it knows such one nickname
  From the pseudonode nickname contained in adjacencies’ hellos, a new DRB can obtain the pseudonode nickname used on this link and reuse it
July 2011
<number>
Pseudonode Nickname

## Slide 12: Control Plane of Pseudonode Nickname
  Pseudonode nickname in LSPs:
  Pseudonode nickname is announced in DRB’s pseudonode LSPs across TRILL campus
  With the help of pseudonode LSPs and the contained pseudonode nickname, other Rbridges can calculate a shortest path to the pseudonode nickname
July 2011
<number>
Pseudonode Nickname

## Slide 13: Contents
Problem Statement
  Traffic fails caused by AF change
Pseudonode Nickname
Control Plane of Pseudonode Nickname
Data Plane of Pseudonode Nickname
TLV Extension for Pseudonone Nickname
July 2011
Pseudonode Nickname
<number>

## Slide 14: Data Plane of Pseudonode Nickname
  Pseudonode nickname is not used for multicast frames, but for unicast data frames:
  Multicast TRILL data frames is forwarded along the given Distribution Tree, which contains all the RBridges in TRILL campus
  So multicast traffic can not fail even if AF has changed;
  Pseudonode nickname influences only ingress and egress RBridges, not transit Rbridges in data plane
July 2011
<number>
Pseudonode Nickname

## Slide 15: Data Plane of Pseudonode Nickname
  Ingress processing:
  Ingress nickname is pseudonode nickname instead of RBridge’s nickname in TRILL header
July 2011
<number>
Pseudonode Nickname
PseNick1
RB3
RB2
RB1
TRILL Campus
H2
H1
RB4
H3
E1
E2
RBx
RBy
When RB1 encapsulates H1’s native data frame into TRILL form, the ingress nickname in TRILL header is PseNick1 not RB1 if the pseudonode nickname function is enabled on link E1

## Slide 16: Data Plane of Pseudonode Nickname
  Egress processing:
  Only VLAN-x forwarder on the destination link can decapsulate the TRILL data frame to native form, and do self-learning
  In the case that the egress nickname in TRILL header is the pseudonode nickname of one connected link, the receiving RBridge should forward it to the VLAN-x forwarder if it is not
  Two methods are given for receiving RBridge to forward the frame:
    Unicasting to VLAN-x AF
    Multicasting to VLAN-x AF
July 2011
<number>
Pseudonode Nickname

## Slide 17: Data Plane of Pseudonode Nickname
PseNick1
RB3
RB1
TRILL Campus
H2
H1
RB4
H4
E1
E2
RBx
RBy
PseNick2
H3
[10]
[10]
[15]
[15]
RB2
RB5
  Egress processing(Unicasting to AF):
  TRILL header unchanged, the Outer.MacDA is replaced with one unicast MAC of VLAN-x AF on the destination link.
July 2011
<number>
Pseudonode Nickname
In this approach, the forwarding table has to be based on {nickname, VLAN}, instead of {nickname}, because RB3 must know which Rbridges on E2 is VLAN-Red AF just from the view of data plane
Egress VLAN next_hop
PseNick2 Red MAC_RB4
PseNick2 Blue MAC_RB5
… … …
D_MAC Egress
H1 PseNick1
… …

## Slide 18: Data Plane of Pseudonode Nickname
PseNick1
RB3
RB1
TRILL Campus
H2
H1
RB4
H4
E1
E2
RBx
RBy
PseNick2
H3
[10]
[10]
[15]
[15]
RB2
RB5
  Egress processing(Multicasting to AF):
  TRILL header unchanged, the Outer.MacDA is replaced with a multicast MAC, i.e., “AF RBridges on this link”
July 2011
<number>
Pseudonode Nickname
The forwarding remains unchanged in form, but a multicast MAC, i.e., “AF RBridges on this link” is required
Only RB4, the VLAN-Red AF, will decapsulate this TRILL data frame to native frame and forward it to H3
Egress next_hop
PseNick2 AF-Rbridges
… … …
D_MAC Egress
H1 PseNick1
… …

## Slide 19: Contents
Problem Statement
  Traffic fails caused by AF change
Pseudonode Nickname
Control Plane of Pseudonode Nickname
Data Plane of Pseudonode Nickname
TLV Extension for Pseudonone Nickname
July 2011
Pseudonode Nickname
<number>

## Slide 20: TLV Extension for Pseudonone Nickname
  Pseudonode Nickname Capability in Hellos
July 2011
<number>
Pseudonode Nickname
The PN bit is used to indicate whether a RBridge supports and enables the pseudonode nickname

## Slide 21: TLV Extension for Pseudonone Nickname
  Pseudonode Nickname TLV
July 2011
<number>
Pseudonode Nickname
This TLV is carried in DRB’s pseudonode LSPs, and the RBridges’ Hellos
Pseudonode nickname record:

## Slide 22: END
July 2011
<number>
Pseudonode Nickname
Hongjun Zhai (ZTE)
Fangwei Hu (ZTE)
Radia Perlman (Intel Labs)
Donald Eastlake 3rd (Huawei)
Notes: <number>
November 2010
TRILL OAM & BFD