## Slide 1: IPv6 Router Advertisement Guard (Ra-Guard) evasion draft-gont-v6ops-ra-guard-evasion
Arturo Servín
LACNIC
81st IETF Meeting, Quebec, Canada
July 24-29, 2011

## Slide 2: Introduction
RFC 6104 introduces the problem statement of Rogue RAs
  Focuses on misconfigured routers
  Mentions different filtering criteria for filtering
  Most basic filtering criterion based on the incomming port for the RA
RFC 6105 specifies RA-Guard
  Focuses on malicious routers (security)
  Very brief Security Considerations section
In many cases RA-Guard has been deployed and seen as a security mechanism
It is a desired feature, since it parallells the DHCPv4-snooping of the IPv4 world

## Slide 3: draft-gont-v6ops-ra-guard-evasion
Describes RA-Guard evasion techniques
Describes more advanced filtering to mitigate them (operational mitigation)
Formally updates RFC 6105 -> the RA-Guard spec is updated such that these issues are addressed
  Enhances the Security Considerations
  Mitigates RA-Guard evasion tehniques

## Slide 4: Evasion technique #1
RA-Guard implementations fail to process the entire IPv6 header chain

## Slide 5: Evasion technique #2
Combination of a Destination Options header and fragmentation:
Original
Packet
First
Fragment
Second
Fragment

## Slide 6: Mitigation:
How to filter RAs:
Follow the entire IPv6 header chain (possibly enforcing a limit on number of Ext. Headers) -- drop the packet if it is an RA or the Ext. Header limit is hit.
If the upper layer protocol is not found (e.g. the packet is fragmented), and the IPv6 Src. Addr. is a link-local address, drop the packet ¥
Else, forward the packet
¥: RAs are required to use a link-local address

## Slide 7: Discussion on the v6ops mailing-list
Was mostly focused on draft-gont-6man-nd-extension-headers
  Related I-D about prohibiting the use of some Ext. Headers with ND
There seemed to be general agreement that these evasion techniques can be mitigated as proposed
Moving forward:
Adopt this I-D as a v6ops wg item?