## Slide 1: Behcet Sarikaya Frank Xia Ted Lemon July 2011
DHCPv6 Prefix Delegation as IPv6 Migration Tool in Mobile Networks IETF 81
http://tools.ietf.org/id/draft-sarikaya-v6ops-prefix-delegation-07.txt

## Slide 2: Changes from -02
Many changes based on comments received
From -06 to -07 in order to remove idnits (Fred asked)
Problem Statement: IPv6 migration is leading to more IPv6 MNs in cellular network and DHCPv6 PD is needed to assign /64s automatically
Draft comes up with three architectures

## Slide 3
DHCPv6 PD for SLAAC
AR is a DHCP Client
DHCP Relay function is needed in AR when DHCP server is not connected directly
Prefixes are delegated to AR through IA_PD Option defined in RFC 3633
AR sends RA containing the prefix(es)
MN configures it’s address using SLAAC

## Slide 4: DHCPv6 PD for Stateful Address Configuration
Stateful address configuration requires a different architecture
AR is DHCP server
MN attach triggers DHCPv6 PD (prefixes received in IA_PD)
MN starts DHCP address request
Server assigns address MN configures it’s address received in IAADDR

## Slide 5: MN as RR
MN may request /64s for additional connections
MN is the requesting router (RR) and sends Solicit with IA_PD
AR is the delegating router (DR) delegates /64s in Reply with IA_PD excluding the default connection

## Slide 6: Next Steps
Ready for WG adoption
Intended status is Informational

## Slide 7
Thank you