## Slide 1: Wireline: Incremental IPv6 draft-kuarsingh-wireline-incremental-ipv6-00
Victor Kuarsingh, Rogers Communications Inc

## Slide 2: Introduction
Draft-kuarsingh-incremental-ipv6 lays out a phased approach to introducing IPv6 in a Wireline Netowrk
  Primary audience would be Cable and other Wireline environments
Intended to help operators whom may be just starting out planning a strategy for IPv6 transition and implementation
Link to framework document [draft-ietf-v6ops-v4v6tran-framework]
Ver. -00 did not have link to RFC6264 but that was suggested
  This draft is more specific and sets out a more definitive phase and objectives

## Slide 3: Version -00 and Future Version -01
Current draft -00 is intended to include more information including
  Operational conditions which may precede, co-exist with and follow each identified phase
  More information on operational considerations for each phase
  More information on which technologies where not listed/used and reasoning
  Overall link to operational environment progress with relation to which technologies are active at each phase.

## Slide 4: Topics Covered (and maturing)
Motivation
Reasons for Phased approach
  Relevance of IPv6 and IPv4 in transition
  IPv4 Resource challenges
  IPv6 Environment Maturity
  Impacts to Operators
Transition Technology Analysis (very basic for novice)
  Auto Tunneling (background)
  CGN (NAT44)
  6RD
  Native Dual Sack
  DS-Lite
  Not mentioned (NAT64, dIVI, A+P etc) – reasoning in next rev

## Slide 5: Approach and Rationale
Introduce IPv6 as soon as possible
  Use Tunneling if needed due to Customer Prem and/or Access network issues
  Assist auto tunneling technologies as best as one can (promotes IPv6 use)
  IPv4 still main service, and aligns with network conditions (tools/mgmt etc)
Mature to Dual Sack as soon as possible
  Use CGN if needed on IPv4 (it’s deployable)
  IPv4 path still independent so less impact to tools, procedures and troubleshooting (environment maturing)
Optimize IPv4 environment
  Move to tunneled IPv4
Keep the most traffic off transition technologies!
Transition techs are “auxiliary paths”, “assist paths”
Relays, translators etc – are engineering and management challenges so use them as little as possible
Use Dual stack phase to move the build of content and services to IPv6

## Slide 6: Transition Phases
Phase 0
  Foundational Items (routing, policy, security, transition architecture)
    Will be expanded in rev -01 with far more detail and operational considerations and input
Phase 1 (Tunneling)
  Managed/Assist Auto-Tunneling (6to4, Teredo)
  Introduce 6RD as early option
  Most tools on Ipv4, main capabilities (content to be added)
Phase 2 (Native Dual Stack)
  Mature IPv6 environment, add in CGN if needed
  Mature IPv6 tools, capabilities, operational proceeds
Phase 3 (Tunneled IPv4)
  IPv6 now mature, services on IPv6 now (for the part)
  Optimize IPv4 (if resourced challenged or if desired)

## Slide 7: Next Steps
Interest and/or value in such a document?
WG Document?