## Slide 1: IPv6 Practices on China Mobile IP Bearer Network draft-chen-v6ops-ipv6-bearer-network-trials-00.txt IETF 81-Quebec, July 2011
G. Chen, T. Yang, L. Li and H. Deng

## Slide 2: Background
China Mobile IPv6 trial program started over 3 years ago
This presentation is mainly focusing on IP bearer network infrastructure for incremental IPv6 deployment
  IPv6 testing on routers was undertaken in our lab before the pre-commercial trials, where there were 7 vendors involved and six months lasted
  With incremental extension, support for IPv6 access network (both mobile and fixed access network) and IPv6 service could be introduced
Trials for IP bearer announced in June 2011, and BRAS will be announced later

## Slide 3: Testing Methodology on IP bearer network trials
Tester
Tester
IP backbone routers
IP core routers
IP access routers
The trial was taken place on hierarchical IP bearer network
Two router testers generate routing information and inject into the under-testing network
Test cases
  IPv6 routing protocol : BGP4+, OSPFv3 and ISIS
  Dual-stack routing protocol
  Tunnel protocol: 6PE/6vPE and configured 6in4 tunnel
  IPv6 ACL, policy routing capabilities and IPsec supporting
  IPv6 routing MIB

## Slide 4: Testing results and observations
Items |  | Results | Observations
IPv6 routing protocol testing | OSPFv3 | OSPFv3 can't establish adjacencies due to inconsistent IPv6 MTU between neighboring routers | The unified MTU configuration is recommended
 | ISIS | OK | MT Routing in IS-IS is recommended to be enable or disable simultaneously
 | BGP4+ | OK | BGP4+ can’t support AS routing loop error processes due to private implementations
Dual-stack routing protocol |  | OK | Routing paths have been computed by IPv4 and IPv6 routing algorithm independently

## Slide 5: Testing results and observations (Cont.)
Items |  | Results | Observations
Tunneling protocol | 6PE/6vPE | OK | The caution has been raised by MTU configuration since intermediate routers would drop big package surpassing network MTU
 | Configured 6in4 tunnel | Routers are failed to support encapsulation package going through MPLS network | 6PE/6vPE are recommended when MPLS is widely enable.
IPsec supporting |  | IPsec capabilities is missing in most routers | It ‘s expected to be supported along with IPv6 deployment
Routing MIB supporting |  | IPv6 MIBs supporting varied significantly from vendor to vendor | Private MIB have appeared to be difficult to build an integrated OAM platform

## Slide 6: Testing Methodology on BRAS
BRAS
BRAS(IPv4)
BRAS(IPv4/iPv6)
L2TP
Case1: BRAS standalone testing
Basic IPv6 protocols supporting
Performance testing
Case2: BRAS networking testing
L2TP tunnel
Subscriber profile management
Notes: <number>

## Slide 7: Testing results and observations
Items |  | Results | Observations
Standalone testing | IPv6 protocol | 1) Can’t integrate DHCPv6 functionalities; 2) Can’t support MLD and PIM/SM | 1) Operator has to build separate DHCPv6 server; 2) multicast-based services are hardly developed
 | Performance testing | 1) IPv6 FIB capacity is only 10% of its IPv4 FIB capacity; 2) Line card throughput is much less than the nominal values when data packages length shorter than 128B | With IPv6 data packages are increasing, it is expected that performance should be upgraded
L2TP networking testing |  | 1) BRAS can’t support IPv6 address delivery through L2TP tunnel; 2) BRAS can’t distinguish IP flow in term of IPv4/IPv6 traffic | 1) IPv6CP signaling is not supported in the case of L2TP tunnel deployed; 2) operator can’t carry out custom charging policy based on different IP families characters

## Slide 8: Summary
In general, the tests on several aspects indicate that the network has basically qualified for IPv6 operations
The community should pay more attentions to increase IPv6 supporting maturity. IPv6 normative features becoming stable & scalable will take more time than you expected
Operators still need to accumulate experiences on IPv6 network configuration and provisioning during the transition period
Comments are welcomed!