## Slide 1
Reserved IPv6 Interface Identifier for Proxy Mobile IPv6
Sri Gundavelli (Cisco)
<number>
<number>
<number>
draft-gundavelli-v6ops-pmipv6-address-reservations-00.txt
IETF 80: NETEXT Working Group – Access Network Information Option for Proxy Mobile IPv6
Notes: <number>
<number>

## Slide 2: Problem Statement
Proxy Mobile IPv6 base specification, RFC 5213, requires the following configuration on every access link.
- the use of a fixed link-layer address
- the use of a fixed interface-identifier
The specification did not reserve any specific addresses for this purpose.
In the absence of any reserved addresses, it is now requiring coordination across vendors and a manual configuration of these addresses on all the mobility elements in a Proxy Mobile IPv6 domain. This is proving to be an operational headache.
Notes: <number>
<number>

## Slide 3: Proxy Mobile IPv6 Domain
PMIPv6 Domain
MN-1
MN-2
LMA
LMAA
Proxy-CoA
LMA
Point-to-Point Link
MAG
MAG
MN-3
PMIPv6 Tunnel
Mobility Entities: LMA & MAG
Transport Network: IPv4/IPv6
MN Addressing: IPv4/IPv6
Tunneling Modes:
- IPv4/IPv6-over-IPv4/IPv6
- IPv4/IPv6-over-IPv4/IPv6-GRE
- IPv4/IPv6-over-IPv4-UDP
Notes: <number>

## Slide 4: Requirements on the Access Link
Proxy Mobile IPv6 protocol requires the MAG to configure the same IPv6 interface identifier, link-layer address and advertise the mobile node’s home network prefixes on every access link, so the mobile node does not detect any change with respect to its layer-3 configuration.
LMA
MAG
Access
Network
MAG
IPv6 Interface Identifier: X (Fixed)
Link-layer Identifier: Y (Fixed)
Global IPv6 Prefixes: IP1, IP2 .. IPn (Fixed)
Notes: <number>

## Slide 5: Proposal
This document proposes the following two IANA actions for reserving a fixed interface-identifier and link-layer address for the use of Proxy Mobile IPv6.
Action-1: This specification reserves an IPv6 interface identifier for Proxy Mobile IPv6 [RFC5213]. This fixed identifier needs to be reserved from the registry, "Reserved IPv6 Interface Identifiers”.
Action-2: This specification reserves a IANA Ethernet unicast address for Proxy Mobile IPv6. This address needs to be reserved from the block. "IANA Ethernet Address block - Unicast Use".
Notes: <number>
<number>

## Slide 6: Next Steps
Propose to take the draft to IESG review for initiating the IANA actions.
Notes: <number>
<number>

## Slide 7
Thank You
Notes: <number>