## Slide 1: Check Point’s World IPv6 Day Experience
Bob Hinden

## Slide 2: Starting Point
No external IPv6 presence prior to World IPv6 Day
Started receiving questions from customers asking if we were going to participate
IT Team had little or no experience with IPv6
We had an ARIN IPv6 allocation

## Slide 3: Planning
Goal to make www.checkpoint.com reachable via IPv6
Worked out rough plan with IT Team
  Mixture of education and planning
  Keep it simple
Set up meeting with local ISC IT Team so our IT folks could talk to IT folks who had done this before
  Many thanks to ISC and Jim Martin

## Slide 4: What we did
Advertized our IPv6 prefix to our ISP (AboveNet) with BGP
Ran dual stack
Used our own Firewalls between the routers and load balancers
We used our existing load balancers to front for the web servers
  Meant we didn't have to touch the actual web servers

## Slide 5: What we learned
It was not as hard as the IT folks initially expected
Our ISP and existing deployed equipment supported IPv6
A few things didn't work in the software releases we were using that we were able to work around
Adding dual stack IPv6 didn't degrade IPv4 service
Load Balancer approached worked well

## Slide 6: Conclusions
We left it up!
Concerns raised about 6to4 brokenness doesn’t seem to be a big concern
  No need to keep a white list
Other organizations may be similar

## Slide 7: QUESTIONS?