## Slide 1: IPv6 Address Accountability Considerations
draft-chown-v6ops-address-accountability-01
IETF81, Quebec
Tim Chown, tjc@ecs.soton.ac.uk
July 28th, 2011

## Slide 2: Rationale
Talking to many (academic) sites introducing IPv6 there is a common concern over lack of IPv6 address accountability due to
  Autoconfiguration
  Multi-addressing
  Privacy addressing
  Potentially rapidly changing addressing
  Hosts being able to pick their own addresses manually with minimal chance of address conflict
Today those sites have accountability with DHCPv4 and, often, Option 82 (RFC 3046)

## Slide 3: Option 1: Switch-router polling
Correlate polled data, including
  IPv4 ARP tables
  IPv6 ND tables
  Switch port MAC tables
Already used by tools like NAV, Netdot
  Could integrate with 802.1X logs, if used
May place load on devices
  Need to poll rapidly enough that device cached data has not expired between polling

## Slide 4: Option 2: Record all ND traffic
Would allow address use to be recorded
Some devices support forwarding function
  e.g. RSPAN, but would need to be specific/filtered
  Regardless, still a lot of traffic – bear in mind ND attacks discussed elsewhere this week
Approach used by NDPmon, RAmond
  Would thus allow more than just address accountability, e.g. rogue RA or DAD DoS detection

## Slide 5: Option 3: Force use of DHCPv6
Use same model as DHCPv4, possibly with RFC 4649 (similar to RFC 3046 for IPv4)
  Not perfect, but the model commonly used now
Issue RAs with M bit set, and Autonomous flag unset such that PIO is not used
  Host should then use DHCPv6
DHCPv6 supports temporary addresses
  Offers privacy addresses with accountability
But may not preclude manual configuration
  If host can determine subnet prefix

## Slide 6: Option 4: Re-use SAVI methods
Not yet discussed in draft
Have noted that logging in SAVI is apparently being encouraged to only record potential IP spoofing events
  i.e. only record the minimum data required for the purpose
  Thus not complete for accountability purposes
Could SAVI be used to record all address usage?

## Slide 7: Questions and next steps?
Privacy concerns are important
  Should privacy be expected *within* a host’s site?
Accountability measures might ideally be independent of address assignment method
Are there Options 5, 6, …?
Is this a topic worth discussing and progressing through a draft?
  Seems to be a very common question raised by sites deploying IPv6 (dual-stack)