## Slide 1: Internet Engineering Task Force
Tuesday July 26, 2011
Mike Ackermann: BCBS Michigan (mackermann@bcbsm.com)
Nalini Elkins: Inside Products, Inc. (Nalini.elkins@insidethestack.com)
RFC for IPv6 IP Identification (IPID) Field
draft-elkins-6man-ipv6-diagnostic-header-00.txt

## Slide 2: TODAY’S AGENDA
IPID FIELD IN IPv4
IPID FIELD IN IPv6 – CURRENT STATE
RECOMMENDATION FOR IPID FIELD IN IPv6
<number>

## Slide 3: IPID FIELD IN IPv4
IPID: Internet Protocol Identification. Provides a unique identifying number for a given IP packet within a flow.
  Sometimes called Datagram number.
Stated Usage
  Enable Fragmentation.
De Facto Usage
  Logically associate packets across complex network situations.
  Of particular value in matching traces taken at multiple points
<number>

## Slide 4: IPID FIELD IN IPv6 – CURRENT STATE
Implemented in Fragment Extension Header (Type 44).
Location:
  32 bit field at offset 4 in FEH.
Issues:
  Only used if Fragmentation required.
  Is a 32 bit field large enough?
  IPID not always available to facilitate network diagnostics. ************
<number>

## Slide 5: RECOMMENDATION FOR IPID FIELD IN IPv6
Implement in Destination Options Extension Header (Type 60).
New Option Type:
  32 or 64 bit field at offset 8 in DOH. (Options Field).
Details:
  Header sent by implementations upon request.
  If sent in Diagnostic Mode, header MUST be ignored by receiver (intended for packet trace systems only).
  New DOH Option is proposed.
  Future: Additional Options could be added for other diagnostic or security purposes as deemed appropriate.
<number>