## Slide 1: 4V6 – stateless 4Via6
http://tools.ietf.org/html/draft-dec-stateless-4v6
W. Dec (wdec@cisco.com)
R. Asati (rajiva@cisco.com)
C. Bao(congxiao@cernet.edu.cn)
H. Deng (denghui@chinamobile.com)
<number>

## Slide 2: Introduction
Motivation for stateless solutions can be found in: draft-operators-softwire-stateless-4v6-motivation
A number of stateless solutions have been proposed.
  4rd, 4v6 (encapsulated or translated mode)
  dIVI-PD (translated mode)
These stateless solutions have shared characteristics; commonly termed stateless 4V6.
  Main differences lies in algorithm and form of transport: v4-v6 Mapped-Encapsulation or v4-v6 Translation
This presentation focuses on the operational considerations of Stateless4V6 and its forms of transport
It also looks at the 4V6 impact when applied to wider industry standard architectures
<number>

## Slide 3: 4V6 IPv6 Address
CE IPv6 subnet is assigned announced via DHCPv6-PD or RA (/64)
  This is NOT in addition to another PD or RA prefix
4V6 index encodes all or part of the IPv4 address + a port index.
<number>

## Slide 4: Stateless 4V6 Translation Mode (example only – NOT numerically accurate)
NAT44
+4V6
NAT
4V6
Gateway
IPv6
IPv4-Private
Customer + IPv6
IPv4-Public
8.8.8.8:80
192.168.0.1:1444
8.8.8.8:80
1.1.1.1:2000
2001:beef:8.8.8.8:80
2001:beef:1.1.1.1.f:2000
8.8.8.8:80
1.1.1.1:2000
NAT44 Source IP Address + Port
Stateless v4-v6 address mapping
Stateless NAT64
1.1.1.1:2000
8.8.8.8:80
1.1.1.1:2000
8.8.8.8:80
192.168.0.1:1444
8.8.8.8:80
Stateless IPv6 to IPv4 mapping (NAT64) + port index
NAPT
2001:beef:1.1.1.1.f:2000
2001:beef:8.8.8.8:80
Done
by CPE
Done
by CPE
4V6 address= 2001:beef:(1.1.1.1.f)::
Index - f = Ports 2000-2999
2001:beef::
Done
by GW
DA:port SA:port
DA:port SA:port
DA:port SA:port
User’s native IPv6 traffic not shown – travels as ships in the night using native IPv6 forwarding

## Slide 5: Stateless46 Mapped Tunnel Mode – (Example only - NOT numerically accurate)
User’s native IPv6 traffic not shown – travels as ships in the night using native IPv6 forwarding
NAPT44
+4V6
NAT
4V6
Gateway
IPv6
IPv4-Private
Customer + IPv6
IPv4-Public
8.8.8.8:80
192.168.0.1:1444
8.8.8.8:80
1.1.1.1:2000
8.8.8.8:80
1.1.1.1:2000
2001:100
2001:beef:1.1.1.1.f
8.8.8.8:80
1.1.1.1:2000
NAPT Source IP Address
MAP IPv4 to IPv6 address + Encap. DA=4rd Gateway Address
Decap packet
4V6 address = 2001:beef:(1.1.1.1.f):
1.1.1.1:2000
8.8.8.8:80
1.1.1.1:2000
8.8.8.8:80
192.168.0.1:1444
8.8.8.8:80
Decap Packet
MAP IPv4 to IPv6 address + index & Encap
NAPT
1.1.1.1:2000
8.8.8.8:80
2001:beef:1.1.1.1.f
2001:100
Done
by CPE
Done
by CPE
Index - f = Ports 2000-2999
Note: IPv4 Port shown for IPv4 packets
Done
by GW
2001:beef::ff
DA:port SA:port
DA SA

## Slide 6: Stateless 46 Comparison Summary

## Slide 7: Operation 4V6 in a 3GPP system
3GPP system functionality is defined to support an extensive set of IP network service requirements,
  Eg Per subscriber QoS, charging, data volume plans.
System is in common deployment. IPv6 fully supported in Release 8/9
Key functionality is the representation and signaling across various interfaces of the user’s virtual connection (Bearer). This is specified in terms of IP Filters.
3GPP currently defines IPv4 & IPv6 traffic filters.
No clearly defined way how to represent IPv4inIPv6 traffic *alongside* regular IPv6 traffic.
  Possible options are an additional (default) bearer (ie additional session), or a new bearer type.
<number>

## Slide 8: Operation 4V6 in 3GPP Characteristics Summary

## Slide 9: Operation 4V6 in a PCMM system
Cable Labs
<number>

## Slide 10: Operation 4V6 in PCMM Characteristics Summary

## Slide 11: Conclusion
No critical technical issues with 4V6 and either the 4V6 mapped-tunnel or translation based modes
  Both approaches represent valid choices
Translated (non encapsulated) transport appears to be operationally less impactful to broader systems and services
  Re-uses native IPv6 network features and system interfaces
  Does not require numerous IPv4 extensions to standard architectures that already support IPv6
Operational impact of both approaches should be documented and trade-offs outlined/clarified.
<number>