## Slide 1: Advanced Requirements for IPv6 Customer Edge Routers
  draft-ietf-v6ops-ipv6-cpe-router-bis-01
IETF 81, Quebec City
July 24-July 29, 2011
v6ops Working Group
Hemant Singh (shemant@cisco.com)
Wes Beebee (wbeebee@cisco.com)
Chris Donley (CableLabs)
Barbara Stark (AT&T)
Ole Troan, Editor (ot@cisco.com) and many other folks from Cable, DSL, Cellular, & Zigbee standards

## Slide 2: Background
Design team consisting of operators, BBF, Cablelabs and IETF participants
  cpe-router@external.cisco.com
RFC6204 “Basic IPv6 CE…”
  Successful!
6204 strategy:
  Punt on anything we don’t know how to do, contentious or hard
“Advanced IPv6 CE” scope:
  “Whatever low hanging fruits left”

## Slide 3: Updates in the -01 version
Removed requirement for ND proxy
Clarified text in the DNS section and removed most text with MAY requirements.
Added a new DHCPv6 requirement – see section 5.7.
  When the WAN interface sends a DHCPV6 SOLICIT message, the CE router SHOULD request all mandatory information (such as IA_NA and IA_PD options) in the SOLICIT regardless of whether any partial information was received in response to previous SOLICITs.
Added new and modified text for 6rd support.
  Clarify support for user configurable, DHCP option 212 support
  6rd hub and spoke mode requirement

## Slide 4: Homenet split
LAN side requirements to homenet
  D-1 (DNS), LMMLD-{1, 2} (MLD), LM-1 (MLD)
  R-1 (Hierarchical PD), Q-1 (QOS)
WAN side requirements in v6ops
  WMLD-1 (MLD)
  DLW-{1,2,3,4,5} (DS-lite)
  6RD-{1,2,3,4} (6RD)
  Q-1 (QOS)
  Transition technology co-existence

## Slide 5: Questions
Split the LAN side requirements off to the homenet WG?
What to do with remaining requirements?
  Abandon?
  Move to softwires as a “transition mechanism interoperate” draft?
  RFC6404: resubmit RFC6204 with the 6rd and DS-lite requirements?
  Continue?