## Slide 1: draft-ietf-abfab-aaa-saml
Josh Howlett, JANET
IETF 82

## Slide 2
SAML RADIUS binding & SAML RADIUS attribute
Abfab Authentication Profile &
Abfab Assertion Request Profile
In SAML, bindings typically use HTTP or SOAP transport. ABFAB is defining a RADIUS binding.

## Slide 3: SAML RADIUS Attribute
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Type | Length | SAML Message...
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 4: SAML RADIUS Binding
SAML requester is RADIUS client / RP
SAML responder is RADIUS server / IdP
SAML protocol message is encapsulated within (and fragmented across multiple instances of) the SAML RADIUS attribute
NAI is used to route RADIUS messages from the SAML requester towards the SAML responder
Attribute is currently defined independently of the Binding, to facilitate use in other contexts – is that actually useful, or a complication?

## Slide 5: Abfab Authentication Profile
A profile of the SAML Authentication Request Protocol that uses the SAML RADIUS binding

## Slide 6: Abfab Assertion Request Profile
TODO
Intend to specify a profile of SAML “Assertion Query and Request Protocol” using the SAML RADIUS binding
Requirements
  Request assertion from authentication IdP, after authentication
  Request assertions from other attribute sources

## Slide 7: Issue: document name
Name includes “aaa”, but only discusses RADIUS
Currently named “A RADIUS Attribute, Binding and Profiles for SAML”
Sufficient?

## Slide 8: Issue: signatures
Use of SAML signatures
  Profile (but not binding) currently prohibits use of SAML signatures
    Encourage use of transport integrity protection, reducing deployment complexity
    Reduce size of SAML messages
  Limited support
  Proposal: require NASes to default NOT to check signatures; and indicate that signatures are not required

## Slide 9: Issue: SAML payload size
RADIUS message MTU of 4kb, but SAML messages can be arbitrarily large
  Option 1: Do nothing
  Option 2: If >4kb, advise deployments to use Diameter
  Option 3: Use a SAML SOAP-based transaction to request attributes or resolve an artifact
  Option 4: Develop a RADIUS-based mechanism to fragment large payloads over multiple RADIUS messages

## Slide 10: Todo
Fix various nits
Define attribute request profile