## Slide 1: Multihop Federations & Trust Router draft-mrw-abfab-multihop-fed-02.txt draft-mrw-abfab-trust-router-01.txt
Margaret Wasserman
mrw@painless-security.com

## Slide 2: Multihop Federations
Drafts describe a mechanism for establishing trust across a multihop ABFAB federation
  Where not all AAA Clients and Servers are connected via a single AAA server
  Replaces current multihop AAA substrate that requires manual configuration at every hop
Introduces a new ABFAB entity called the Trust Router
  Trust router and KNP are combined to provide support for multihop federations

## Slide 3: Trust router protocol
eu
us
ca
uk
Announce eduroam: ja.net
ja.net

## Slide 4: RADIUS substrate
Trust router
Trust Router allows path selection through the AAA fabric
Eliminates need for manual configuration at each hop
AAA client
AAA server
Relying party
domain
Identity Provider
domain

## Slide 5: Community of Interest (CoI)
Conceptually: A set of users (Principals) and Services
Technically: Set of IdPs, Relying Parties and Trust Routers
Each CoI results in a separate routing tree, as paths must traverse nodes that are part of the right community
Desire to support many Communities of Interest using a shared set of infrastructure and credentials
Dynamic Trust Router makes it practical to support many Communities of Interest that come and go through a lightweight creation process

## Slide 6: Trust Link
A Trust Link represents an available KNP hop between a Trust Router and and another Trust Router or a AAA Server
A Trust Link is an assertion that a Trust Router is willing to provide temporary identities to access another element in the ABFAB system
  Another Trust Router
  Or a AAA Server (Radius, RadSec or Diameter)
Shown as a realm name and realm name (type), separated by an arrow
  A->B(T) indicates there is a Trust Link from realm A to a Trust Router in realm B
  ja.net -> oxford.ac.uk(R) indicates there is a Trust Link from ja.net to a AAA Server in oxford.ac.uk

## Slide 7: Trust Path
A Trust Path is a series of KNP hops that can be used to reach a AAA server in a destination realm
Each hop across the substrate is called a Trust Link
Shown as series of realms and types, connected by arrows
  Currently defined types are Trust Router (T) or AAA Server (R)
  Example: A -> B(T) -> C(T) -> D(T) -> D(R)

## Slide 8: Trust Router Functions
Trust Router Protocol
  Distributes information about available Trust Links in the network
  Calculates a tree of Trust Paths to reach target destinations
Trust Path Query
  Provide “best” path to a destination realm in response to queries from local RPs
Temporary Identity Request
  Provision temporary identities that RPs can use to reach the next hop in the Trust Path, in response to KNP requests from RPs

## Slide 9: Trust Router Protocol
Exchange information about Trust Links between Trust Routers
  Trust Links are unidirectional and of a specific type
    A -> B(T) does not imply A -> B(R), B -> A(T) or B -> A(R)
  Realm names are not necessarily hierarchical, but they may be
    example-u.ac.uk is not necessarily reached via .uk or .ac.uk
Tree of available Trust Paths rooted in local realm is calculated by each Trust Router

## Slide 10: Trust Router Messages
Hello Message
  Exchanged between neighboring Trust Routers to establish adjacency and perform authentication
Trust Link Database Message
  Used to send a full database when needed
Trust Link Update Message
  Used to send incremental database updates
All messages encoded in JSON over TCP, with GSS-API-based security

## Slide 11: Compact Tree Representation
Trees (and subtrees) are represented as an ordered list of Trust Links (depth first traversal)
Each entry contains
  Index: Depth of this node in the tree
  Target Entity: Type and Target of this link
  CoIs: The CoIs to which this link applies
Start of link is implied by location in the tree

## Slide 12: Trust Path Query
Generated by an RP to request a Trust Path to reach a AAA server in a destination realm
When a Trust Path Query is received, the Trust Router:
  Authenticates the RP, and checks local policy to determine whether or not to reply
  Searches its tree of Trust Paths to find the best path to reach the destination
  Returns the best path, if found, to the RP

## Slide 13: Questions? Feedback?
Questions about what we are proposing?
Feedback on this proposal?
Next Steps:
  WG Chairs have suggested that we start with a problem statement document. Thoughts?
  Who is interested in helping us with this work?
    Review documents, contribute text, etc.