## Slide 1: RTCP SDES SRCNAME
Magnus Westerlund
Bo Burman
Patrik Sandgren
draft-westerlund-avtext-rtcp-sdes-srcname-00

## Slide 2: Overview
General Problem
Use Cases
Related Solutions
Proposal
Way Forward

## Slide 3: General Problem
Associating multiple SSRCs related to a single media sources:
  Media source are: Camera, Microphone, Keyboard, Mixes of the Media, Media compositions, Conceptual Source (like video of most active speaker)
  SSRCs may be in same or different RTP sessions
  CNAME is not sufficient when a end-point has multiple media sources in any given RTP session that needs associating
For streams in different RTP sessions, requiring the same SSRC over multiple Sessions could be used
  Forces SSRC collision to change in all sessions
  Same SSRC can’t be used when streams are in the same session
Should be possible to use in all use cases where this RTP/RTCP mechanism is needed

## Slide 4: Use Cases
RTP Retransmission with SSRC multiplexing
  Determines association between source and retransmission by matching NACK to Retransmitted packet based on sequence number
  Limitation that end-points can’t have multiple outstanding retransmission request before association is established.
  Not guaranteed to work in group communication cases
Simulcasting different version of the same stream
  draft-westerlund-avtcore-rtp-simulcast-00
  Different alternative encodings of the same source needs to be associated
SVC using Multi-session Transport
  Underspecified but appear to rely on same SSRC over multiple sessions to associate different layers
Forward Error Correction
  Needs to associate the FEC data with source stream(s)

## Slide 5: Related Solutions
SSRC-Group (RFC5956)
  Defined in SDP
    Thus requiring SDP based signaling
    Not suitable for RTP sessions with dynamic numbers of senders
  Associate SSRCs in the same session
  Good complement for grouping as it is in signaling
SDP Grouping Framework (RFC 5888)
  Groups two m= lines, commonly different RTP sessions
  Only defines how RTP sessions are grouped
  Likely to be used to indicate the relation of the RTP sessions when association of SSRCs in different RTP sessions are needed.

## Slide 6: RTP/RTCP General Solution
Draft authors believe a general solution in the RTP session rather than on signaling only would be a useful tool
What are the interest in the WG for the general problem?

## Slide 7: Proposal
Define a new SDES Item: SRCNAME
  A label per media source on a end-point
  All associated media streams have the same label
  The label is recommended to be a version of the randomized version specified by “Guidelines for Choosing RTP Control Protocol (RTCP) Canonical Names (CNAMEs)" (RFC6222) by including an enumeration of the end-points streams before hashing.
Define how to use it with SDP Source attribute (RFC5576)
  Enables early binding in SDP when appropriate

## Slide 8: Way Forward
We would like to go forward to specify a general solution
We don’t plan to go back fixing the identified cases with short comings ourselves
Interest in the proposed solution?