## Slide 1: RTP Media Stream Pause and Resume
Magnus Westerlund
Bo Burman
Daniel Gröndal
Azam Akram
draft-westerlund-avtext-rtp-stream-pause-00

## Slide 2: Introduction
Use Case
Requirements
Why not use TMMBR?
Proposal

## Slide 3: Use Case
Point to Point
  Receiver is currently not playing out the media stream due to minimized UI for example
RTP Mixer Topologies with a number of session participants
  The RTP mixer selects, composes or mixes a number of participants into a outgoing media streams
  Each participant may receive a different combination of incoming streams
  In some cases one or more stream sent to the mixer is not used
  Any unused stream wastes resources
  Temporarily disable streams until need
    Voice activity / automatic selection system
    User controlled selection
Simulcast of multiple encoding alternatives results in more streams that may not be currently used
A
Mixer
B
C
D

## Slide 4: Requirements
Allow an RTP Node to temporarily disable delivery of an identified media stream
Quickly resume media delivery to maintain real-time behavior
A mistake in classifying the RTP topology should not cause impact on other session receivers
Must handle joining receivers so that they are fooled to believe a media stream is silent on its own choice rather than being paused
Ensure that basic RTP/RTCP mechanism don’t get screwed up

## Slide 5: Why not TMMBR
It has been raised that Temporary Maximum Media Bit-rate Request (TMMBR) [RF5104] with a value equal to 0 can be used for this mechanism
TMMBR Semantics has some issues
  If the media stream is shared between multiple receivers a TMMBR=0 will cut off the other that hasn’t requested to pause the stream
  A new session participant will not know that a paused SSRC even is paused, rather than not an active sender
  When setting TMMBR > 0 the current semantics mandate a consideration time to allow others from preventing the value to increase
    Causes significant delay to resume if honored

## Slide 6: Proposal
Define a new RTCP AVPF Transport Layer Feedback message that allows to
  A requesting SSRC to request state at the media sender to pause
  A requesting SSRC to request resume
  An Acknowledgement message indicating
    if pause will happen
    if there additional receivers on the same media leg not having set state
    Resume indication
  Pause happens when all known SSRC sending RTCP RR has established PAUSE state
  The media will resume as soon as not all SSRC have established state
    New receiver joins
    Anyone sends a Resume request

## Slide 7: Proposal
Pause and Resume requests are not allowed on CSRCs
The semantics of what that would mean
  If RTP mixer delivers multiple streams, would a pauses CSRC exclude it from any stream, or just the currently used ones
  Please compare with Media Stream Selection
    draft-westerlund-dispatch-stream-selection-00
    Have include, exclude and reset semantics
    Can scope requests to particular delivery media streams

## Slide 8: Next Steps
What are the interest for the general problem?
Additional related use-cases?
Interest in the proposed solution?