## Slide 1: Revision of the Binary Floor Control Protocol (BFCP) for use over an unreliable transport (draft-sandbakken-dispatch-bfcp-udp-03)
Charles Eckel, Tom Kristensen, Mark Thompson, Geir Arne Sandbakken, Eoin McLeod
IETF 82 BFCPBIS WG Meeting
November 16, 2011

## Slide 2: Motivation
Existing deployments of SIP based videoconferencing typically:
  Consist of RTP media streams for audio and video
  Use ICE and/or other methods for NAT/firewall traversal
  Found in enterprise networks
When enhancing with support for content sharing, the BFCP connection often poses a problem
  There may be a strong preference for UDP based signaling in general
  Establishment/traversal of the TCP connection involving ephemeral ports, as is typically the case with BFCP over TCP, can be problematic
This draft defines UDP as an alternate transport for BFCP, leveraging the mechanisms in place for RTP over UDP media streams for the BFCP communication
IETF 82 BFCPBIS WG Meeting, Nov. 16, 2011
<number>

## Slide 3: Approach
Minor changes to transaction model
  All requests now have a response to complete transaction
    Added an explicit “Ack” primitive for each case in which none existed
  Retransmission timer to ensure reliability
  Transaction Initiator flag to indicate a primitive is a response to a previous request
  One pending transaction per entity (ordering, congestion control)
<number>
IETF 82 BFCPBIS WG Meeting, Nov. 16, 2011

## Slide 4: Approach (cont)
Goodbye/GoodbyeAck dissociate (TCP/BFCP close)
New ERROR-CODEs for following cases:
  Unable to parse message
  Use DTLS
DTLS MUST be supported
ICE/STUN if applicable and needed
<number>
IETF 82 BFCPBIS WG Meeting, Nov. 16, 2011

## Slide 5: Open Items
DTLS connection establishment
Request Specific ACK vs. Generic Ack
Large Message Considerations
BFCP/STUN demultiplexing
<number>
IETF 82 BFCPBIS WG Meeting, Nov. 16, 2011

## Slide 6: DTLS Connection Establishment
Which party, the client or the floor control server, acts as the TLS/DTLS server depends on how the underlying TCP/DTLS connection is established. For example, when the TCP/DTLS connection is established using an SDP offer/answer exchange [RFC4583], the answerer (which may be the client or the floor control server) always acts as the TLS/DTLS server.
<number>
IETF 82 BFCPBIS WG Meeting, Nov. 16, 2011

## Slide 7: DTLS Connection Establishment: Options
The answerer always acts as the TLS/DTLS server, per RFC 4583 (as currently defined)
The BFCP server always acts as the TLS/DTLS server
The offerer always offers setup:actpass and the answerer answers either setup:active or setup:passive, where setup:active is RECOMMENDED (per RFC 5763 and as posted to bfcpbis mailer http://www.ietf.org/mail-archive/web/bfcpbis/current/msg00007.html)
Preferred option: (3)
  Adheres to RFC 5763, does not overload offer/answer semantics, works for offerless INVITE with B2BUAs
<number>
IETF 82 BFCPBIS WG Meeting, Nov. 16, 2011

## Slide 8: Request Specific ACK vs. Generic ACK
RFC 4582 primitives in BLUE, new primitives in GREEN ITALICS
FloorRequest / FloorRequestStatus / [FloorRequestStatusAck]
FloorRelease / FloorRequestStatus / [FloorRequestStatusAck]
FloorRequestStatus / FloorRequestStatusAck
FloorRequestQuery / FloorRequestStatus / [FloorRequestStatusAck]
UserQuery / UserStatus
FloorQuery / FloorStatus / [FloorStatusAck]
FloorStatus / FloorStatusAck
ChairAction / ChairActionAck
Hello / HelloAck
Error / ErrorAck
Goodbye / GoodbyeAck
<number>
IETF 82 BFCPBIS WG Meeting, Nov. 16, 2011

## Slide 9: Request Specific ACK vs. Generic ACK: Options
Always send request specific ACK (as currently defined)
Send request specific ACK only if transaction initiator flag indicates message is initiating a new transaction
Send a generic ACK at the transport level for every message that exists in RFC 4582
Preferred option: (1)
  (2) reduces number of ACK but requires passing of transaction initiator flag through the protocol stack
  (3) simplifies the existing transaction model as well as the adding of future BFCP primitives, but more chatty protocol and more churn of existing implementations
<number>
IETF 82 BFCPBIS WG Meeting, Nov. 16, 2011

## Slide 10: Large Message Considerations
Large messages become a concern when using BFCP if the overall size of a single BFCP message exceeds that representable within the 16-bit Payload Length field of the COMMON-HEADER.
When using UDP, there is the added concern that a single BFCP message can be fragmented at the IP layer if its overall size exceeds the MTU threshold of the network.
The target use cases for BFCP via UDP typically involve relatively small BFCP messages ... BFCP entities SHOULD ensure that their messages are smaller than the recommended MTU size of 1300 bytes when encoded to minimize the likelihood of fragmentation in route to their peer entity.
<number>
IETF 82 BFCPBIS WG Meeting, Nov. 16, 2011

## Slide 11: Large Message Considerations: Options
Leave as out of scope (as currently defined)
Add a mechanism for splitting a single large message into additive messages
  The mechanism defined for RELOAD in section 5.7 of [I-D.ietf-p2psip-base] has been identified as a good candidate.
Add an applicability statement on those BFCP messages and/or attributes deemed as inappropriate for use over transports where fragmentation is a concern
Define SIP event package to deliver information
Preferred option: (1)
  Not an issue for existing deployments/intended use cases
<number>
IETF 82 BFCPBIS WG Meeting, Nov. 16, 2011

## Slide 12: BFCP/STUN Demultiplexing
In order to facilitate the initial establishment of NAT bindings, and to maintain those bindings once established, BFCP over UDP entities are RECOMMENDED to use STUN [RFC5389] for keep-alives, as described for SIP [RFC5626].
Consequently, implementations need to be able to demultiplex incoming BFCP/STUN packets
<number>
IETF 82 BFCPBIS WG Meeting, Nov. 16, 2011

## Slide 13: BFCP/STUN Demultiplexing: STUN
Format for STUN messages:
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|0 0| STUN Message Type | Message Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Magic Cookie |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
| Transaction ID (96 bits) |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
The most significant 2 bits of every STUN message MUST be zeroes. This can be used to differentiate STUN packets from other protocols when STUN is multiplexed with other protocols on the same port.
<number>
IETF 82 BFCPBIS WG Meeting, Nov. 16, 2011

## Slide 14: BFCP/STUN Demultiplexing: BFCP
Format for BFCP messages:
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Ver |I| Res | Primitive | Payload Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Conference ID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Transaction ID | User ID |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
The “I” field is added by draft-sandbakken-dispatch-bfcp-udp.
But per RFC 4582 as well as draft-sandbakken-dispatch-bfcp-udp:
Ver: The 3-bit version field MUST be set to one (i.e. 001) to indicate this version of BFCP.
Therefore, as with STUN, the first two bits are always zeroes.
<number>
IETF 82 BFCPBIS WG Meeting, Nov. 16, 2011

## Slide 15: BFCP/STUN Demultiplexing: Options
Leave as currently defined
  A reasonable STUN (RFC 5389) implementation will also check the magic cookie (0x2112A442) and check if the message length is sane (i.e. STUN messages are padded to a multiple of 4 bytes, the last 2 bits of this field is always zero)
Change the version number for BFPC [via UDP] to a value where one of the first two bits is one
Preferred option: (1)
  While changing the version number may be desirable in the future for other reasons, STUN demultiplexing is not viewed as a sufficient justification for such a change.
<number>
IETF 82 BFCPBIS WG Meeting, Nov. 16, 2011

## Slide 16: THANK YOU
Charles Eckel, Tom Kristensen, Mark Thompson, Geir Arne Sandbakken, Eoin McLeod
IETF 82 BFCPBIS WG Meeting
November 16, 2011