## Slide 1: Routers convergence benchmarking
draft-papneja-bgp-basic-dp-convergence-02
draft-varlashkin-router-conv-bench-00
Ilya Varlashkin ilya@easynet.com
Rajiv Papneja rajiv.papneja@huawei.com
Bhavani Parise bhavani@cisco.com
Dean Lee dlee@ixiacom.com
Sue Hares skh@ndzh.com

## Slide 2: Current status
draft-papneja-bgp-basic-dp-convergence-02
  data-plane only
  assumes fwd ability implies BGP convergence
draft-varlashkin-router-conv-bench-00
  mentioned @IETF81, now published
  works with independent data- and control-planes
The two drafts complement each other

## Slide 3: Two drafts side-by-side
draft-papneja-bgp-basic-dp-convergence-02 | draft-varlashkin-router-conv-bench-00
Assumes: FWD ability == protocol converged | Assumes forwarding ability and protocol convergence are independent
Data-plane measurement | Data-plane for forwarding ability, control-plane for (protocol) status propagation
Covers BGP setup; IGP is out of scope | Primarily intended for BGP + some IGP, with or without MPLS
Tests: RIB-In, RIB-Out, iBGP, eBGP (direct and multi-hop) | Tests: intrinsic delays of the test setup, generic data-plane, generic control-plane. Both iBGP and eBGP can be tested.
Failure scenarios: Physical link failure on DUT/Remote end, ECMP Link failure on DUT end, BGP session failure, BGP hard reset, BGP soft reset, BGP route withdrawal, BGP Path attribute change, BGP Graceful restart | Failure scenarios: direct link failure with and without LoS, non-direct link failure, next-hop failure, best route withdrawal.

## Slide 4: Work roadmap
Reality alignment
  ensure methods deliver values that people want to know
  assert feasibility
Fine-tune methodology
  eliminate (most of) dependency on non-DUT
  define equipment config in generic terms
Sort out terminology

## Slide 5: Test topology
DUT
R1
R2
R3
R4
NetA
M1
[S]
ER1
ERn
1
1
9
C2
C1
3
2
NetB1
NetBn

## Slide 6: TODO list
Agree on approach
Do we need to change test topology?
Do we need to change failure scenarios?
Input welcome!
Aim for WG-item readiness by next IETF
Consider need for amending RFC4098