## Slide 1: Framework for G.709 Optical Transport Network (OTN)
draft-ietf-ccamp-gmpls-g709-framework-05
CCAMP WG, IETF 82nd Taipei
Notes: <number>

## Slide 2: Content of the drafts
Informative overview of the OTN layer network
Connection management in OTN
GMPLS and PCE requirements
  Hierarchy LSP in OTN
  GMPLS Signaling extension requirements
  GMPLS Routing extension requirements
  GMPLS LMP extension requirements
  PCEP requirements
Notes: <number>

## Slide 3: Changes from version 04
Refined some text related to the need to define a new Switching Capability value (101) specific for OTN (introduced in the routing draft)
Added a new signaling requirement for consistency between the Switching Type in the signaling of LSPs (G7099-V3) and the new Switching Capability defined in routing
Added a new routing requirement about TSG advertisement, and consequently, refined some text about TSG information in the signaling.
Refinement regarding link bundling in alignment with routing draft.
Notes: <number>

## Slide 4: Next Step
Refine the document by constant monitoring the progress of OTN data plane tech
Consistent with [OTN-Info] and protocol drafts (e.g. TSG discussion)
Refine the draft based on possible new requirement coming from the meeting or mailing list
Notes: <number>

## Slide 5
draft-ietf-ccamp-otn-g709-info-model-02
CCAMP WG, IETF 82nd Taipei
Information model for G.709 Optical Transport Network (OTN)
Notes: <number>

## Slide 6: Content
Information needed in signaling and routing against OTN requirements provided in [OTN-Fwk]
Analysis of the current protocol capabilities and requirement for extension in support of the indicated information requirements.

## Slide 7: Changes from version .00 to .02
Version 04 of draft-bccg-ccamp-otn-g709-info-model has become a WG from Prague meeting. Version 00 of the WG document
Version 00  01
    new text for Tributary Slot Granularity and added sub-Chapter for fall-back procedure
    Update routing and signaling requirement accordingly to [OTN-FWK]
    Added text and example for multi-stage multiplexing advertisement of intermediate layer
Version 01  02 updated section 4.1 on Tributary slot granularity with examples and new text to clarify information requirement.
Notes: <number>

## Slide 8: Tributary slot granularity information
ODU3-LSP
ODU2-LSP
TSG-server
TSG-client
TSG-client  it is the TSG that the endpoints of the link or hierarchical LSP export to their clients . In this case the TSG that ODU2-LSP signals and exports to clients .
  TSG is applicable only to ODU clients being a characteristics of the ODTUk.ts and ODTUjk adaptations
TSG-server  it is the TSG used to map an E2E ODUj onto the ODUk links or hierarchical LSPs on its path. In the figure above is how the ODU2-LSP is mapped in the structured ODU3-LSP. It can be retrieved by the field “length” of the label format together with Traffic parameters (Signal Type) and type of ODU link (IF-ID RSVP_HOP).

## Slide 9: Example : TSG information need
OTU2
ODU3 LSP
ODU2-LSP
At ODU2 LSP setup , the TSG-server can vary along the path .
ODU2 LSP exports towards his client (e.g. ODU0 in the figure) TSG capability = 1.25
If ERO does not provide interface identifier, penultimate hop node has to check TSG information to select the correct interface to guarantee that adaptation capability “on output” matching the adaptation capability of the ingress
ODU3 LSP
OTU2
OTU2
TPN=x
reserved
length=16
X
0
0
Padded bits
ODU3 LSP exports 2.5 TSG capability
TPN=x
reserved
length=32
X
0
0
ODU3 LSP exports 1.25 TSG capability
A
B
C
D
E
F
ODU0-LSP
TSG-client=1.25
TSG-client=1.25
1.25
2.5
1.25
1.25
2.5
This adaptation must not be selected because it is at 2.5
TSG-server=2.5
TSG-server=1.25

## Slide 10: Example : Client information need
OTU2
ODU3 LSP
ODU2-LSP
The signaled TSGs information is not enough to have a complete choice
since the penultimate hop node has to distinguish between interfaces/FA-LSP
with the same TSG (e.g. 1.25Gbps) whether the interface is able to
support the right hierarchy.
ODU3 LSP
OTU2
OTU2
A
B
C
D
E
F
ODU0-LSP
TSG-client=1.25
TSG-client=1.25
1.25
1.25
1.25
1.25
1.25
This adaptation must not be selected because it does not support correct hierarchy
TSG-server=2.5
TSG-server=1.25
ODU0ODU2
ODU1ODU2

## Slide 11: Requirements
To select correct forwarding interface
If auto-payload type is on, an information related to the client supported (client hierachy) could be enough for the right choice
If auto-payload type is off, a further information related to TS granularity supported by the interface is needed.

## Slide 12: Next steps
The draft will be updated after the meeting splitting TSG section in two:
  one for data plane aspect (payload type and TSG relationship, fall-back procedure )
  the other the control plane part , practically the present part (apart possible refinement needed)
Refining the draft based on feedback of the meeting and possible further requirement coming from G.709 and related work
Notes: <number>