## Slide 1: RSVP-TE Extensions to Exchange MPLS-TP LSP Identifiers
CCAMP/MPLS WG, IETF 82th, Taipei
draft-zhang-ccamp-mpls-tp-rsvpte-ext-tunnel-num-01
Fei Zhang
Xiao Bao
Notes: <number>

## Slide 2: Problem Statement
Mis-Connectivity Defect (RFC6371)
A sink MEP identifies a mis-connectivity defect based on the comparison of the expected MEP_ID (pre-stored) and received MEP_ID (inserted in the proactive CC-V OAM packet) .
A1/Z9 needs to configure each other’s MEP_ID before sending the proactive CC-V OAM packet
The format of the MEP_ID : Global_ID::Node_ID::Tunnel_Num::LSP_Num (RFC6370)
Gap Analysis
Statically configured LSPs, A1/Z9 can configure each other’s MEP_ID by GAP messages (draft-fbb-mpls-gach-adv-00)
Dynamically established LSPs
  A1 needs to configure the tunnel number configured at Z9 node (co-routed bidirectional LSP)
  A1/Z9 needs to know each other’s Global_ID (co-routed/associated bidirectional LSP)
  The above information are not covered by the current signaling protocol
Focusing on the control plane solution
Notes: Arbitrary spectral resource can be allocated to a channel acceding to the signal bitrate leading to
<number>

## Slide 3: Protocol Extensions
LSP_ATTRIBUTES object
  LSP Attribute Flags, one new bit defined: “LSP identifier indication”
  Two new TLVs
    Connection TLV (appear in Path/Resv message of co-routed bidirectional LSP)
      L bit is set, The value carried in “Destination Tunnel Num” must be configured at Z9
      L bit not set, “Destination Tunnel Num” can be empty/filled by the recommended value
0 1 2 3 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ | Type (TBD) | Length | +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ |L| Reserved | Destination Tunnel Num | +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Global_ID TLV
  For co-routed bidirectional LSP, it can appear in Path/Resv message
  For associated bidirectional LSP, only appears in the Path message
0 1 2 3 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ | Type (TBD) | Length | +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ | Global_ID | +-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Thanks George, Lou, Venkatesan, Jaihari, and Muliu for the discussion of the solution
Notes: <number>

## Slide 4: Next Steps
Updated based on the discussions
  Be individual?
  As an input to draft-ietf-ccamp-rsvp-te-mpls-tp-oam-ext-07 ?
Comments/Feedback?
