## Slide 1: draft-sun-ccamp-gmpls-perf-mib
Weiqiang Sun

## Slide 2: Background
When LSPs are provisioned dynamically through GMPLS/MPLS-TE networks, it is useful to know the performance of the provisioning process (setup/release performance)
  To provide information for applications like BoD (think about the delay performance measurement in IP networks)
  To understand how the control plane performs when a large number of LSP are provisioned

## Slide 3: Finished and on-going efforts
RFC 5814
  performance metrics and measurement methodologies from a pure control plane’s perspective
draft-ietf-ccamp-dpm
  Performance metrics and methodologies considering data path consistency/conformity
Both defined for active measurement
  Benchmarking or field trial
  But may not be suitable for operational networks

## Slide 4: Purpose of this work
To monitor the run-time setup/release performance of the control plane
  In operational networks
  Do this in a passive manner, i.e., store the information when real-life connections are established/released
Such information may be retrieved and monitored through the NMS
Provide a means to identify possible provisioning performance degradation, or mal-functioning

## Slide 5: Examples of performance degradation (I)
Provisioning performance degrades gradually.

## Slide 6: Examples of performance degradation (II)

## Slide 7: Ways of doing this
Record the timestamps of initiation (Ti) and completion (Tc) during the connection provisioning process
Along side a status flag: InProgress/Up/Deleted
Actual setup/release delay for Up or Deleted connections:
Not recording the value of T!
  To handle failure cases, e.g., when a setup attempt does not finish at all.
  T= Tc – Ti

## Slide 8: MIB structure
Two top level objects
  gmplsPerfTunnelConfigured
    # of recorded performance entries
  gmplsPerfMaxEntries
    Maximum # of entries
One table
  gmplsPerfTable
    Each entry in the table records the timestamps of one provisioning process

## Slide 9: To be discussed
Currently it is mapped to/extending gmplsTeStdMIB (RFC 4802)
  More comfortable to be discussed in CCAMP, where previous performance related documents have been rooted
Mapping it to RFC 3812 (MPLS-TE-STD-MIB) is also an option
  But have to be moved to MPLS WG?

## Slide 10: Thanks!
Weiqiang Sun