## Slide 1: GMPLS OSPF-TE Extensions in support of Flexible-Grid in DWDM Networks
CCAMP WG, IETF 82nd, Taipei, Taiwan
draft-zhang-ccamp-flexible-grid-ospf-ext-00.txt
Fatai Zhang (zhangfatai@huawei.com)
Xiaobing Zi (zixiaobing@huawei.com)
Ramon Casellas (ramon.casellas@cttc.es)
O. Gonzalez de Dios (ogondio@tid.es)
D. Ceccarelli (daniele.ceccarelli@ericsson.com)

## Slide 2: Objective
Defines OSPF-TE extensions in support of GMPLS control for Flexible-Grid

## Slide 3: What information to be advertised?
WSON related information (except wavelength availability) (See [draft-ietf-ccamp-rwa-info-13])
  (old) Node info: Connectivity Matrix, Signal Compatibility (FEC Type, Modulation Type, Resource Pool…)
  (old) Link info: Administrative Group, SRLG, Link Protection Type, TE Metric, Port Restrictions…
(new) Available Frequency Ranges of each link (Link information)
  This is the significant difference between WSON(fixed grid) and flexi-grid. See next slide.
  This draft focuses on this information.

## Slide 4: Compared to WSON
DWDM link
Flexible Grid
0
1
2
3
4
5
6
7
8
9
-9
-8
-7
-6
-5
-4
-3
-2
-1
Flexi-LSP1: Frequency Slot 1 (37.5 GHz width)
Flexi-LSP2: Frequency Slot 2 (50 GHz width)
...
…
DWDM link
50 GHz fixed Channel Spacing
0
1
2
3
4
-4
-3
-2
-1
193.1 THz
...
…
λ0
λ1
λ2
λ3
λ-4
λ-3
λ-2
λ-1
WSON (Fixed Grid):
each wavelength has a pre-defined central frequency and all the wavelengths occupy the same frequency range (channel spacing)(one of 12.5GHz,25GHz, 50GHz, 100GHz).
All the wavelengths in the DWDM links can be identified uniquely and the status (available or not) of the wavelengths can be advertised.
Flexi-Grid: the slot width of the wavelengths are flexible on a flexible-grid DWDM link (ie. the slot width is uncertain before a frequency slot is allocated), so the available frequency ranges instead of the specific "wavelengths" should be advertised

## Slide 5: Available Frequency Ranges
DWDM link
0
1
2
3
4
5
6
7
8
9
-9
-8
-7
-6
-5
-4
-3
-2
-1
Available Frequency Range 1
Available Frequency Range 2
193.1 THz
...
…
Note: The frequency slots of the LSC flexi-LSPs on a fiber must not overlap with each other, so the frequency slots of the existing flexi-LSPs are unavailable frequency ranges for other flexi-LSPs.
Used
The available resource (ie., available frequency ranges) of each Flexi-Grid link MUST be advertised.

## Slide 6: Extensions
The Available Labels Set sub-TLV defined in [GEN-OSPF] is re-used to advertise the available frequency ranges for the flexible-grid DWDM links.
Available Labels Set sub-TLV (Inclusive/Exclusive Label Range)
Label format defined in [flexible-grid-rsvp-te-ext]
No “m”, because the value of “m” is uncertain before a frequency slot is allocated
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|2 or 3 | Num Labels(not used) | Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Start Label |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| End Label |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|Grid | C.S. | Identifier | n |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
Action=2,3 means inclusive or exclusive

## Slide 7: Example 1: Exclusive
DWDM link
0
1
2
3
4
5
6
7
8
9
-9
-8
-7
-6
-5
-4
-3
-2
-1
Unavailable Frequency Range 1
Unavailable Frequency Range 2
193.1 THz
...
…
<Available Labels> sub-TLV:
Exclusive Range 1: [Start label = 193.1 + (-8)*0.00625,
End Label = 193.1 + (-2)*0.00625]
Exclusive Range 2: [Start label = 193.1 + 0*0.00625,
End Label = 193.1 + 8*0.00625]
A frequency slot of a flexi-LSP is determined by the central frequency and slot width :
Lowest frequency = (central frequency) - (slot width)/2
= (193.1 + n * 0.00625) - (0.0125 * m)/2
= (193.1 + (n - m) * 0.00625) THz;
Highest frequency = (central frequency) + (slot width)/2
= (193.1 + n * 0.00625) + (0.0125 * m)/2
= (193.1 + (n + m) * 0.00625) THz;

## Slide 8: Example 2: Inclusive
DWDM link
0
1
2
3
4
5
6
7
8
9
-9
-8
-7
-6
-5
-4
-3
-2
-1
Available Frequency Range 1
Available Frequency Range 2
193.1 THz
...
…
<Available Labels> sub-TLV:
Inclusive Range 1: [Start label = 193.1 + (-8)*0.00625,
End Label = 193.1 + (-2)*0.00625]
Inclusive Range 2: [Start label = 193.1 + 0*0.00625,
End Label = 193.1 + 8*0.00625]

## Slide 9: Open Discussions
How to deal with bandwidth (bit rate in bps) per priority and other bandwidth sub-TLV(e.g., Unreserved Bandwidth, Maximum Bandwidth…)?
  It seems that the bandwidth in bps is meaningless in flex-grid (fixed-grid as well ?)
  The only resource is the available frequency ranges on each link
  Your opinions?
Does it need to define a new switching type for flexi-grid(ie., different from WSON)?
  Not quite sure

## Slide 10: Next Steps
Coordinate with WSON work
Refine it according to the feedback from the meeting or mailing list