## Slide 1: OSPF-TE Extensions for Flex-grid
Abinder Dhillon (adhillon@infinera.com)
Iftekhar Hussain (ihussain@infinera.com)
Rajan Rao (rrao@infinera.com)
Marco Sosa (msosa@infinera.com)
draft-dhillon-ccamp-super-channel-ospfte-ext-01.txt
IETF 82 - Taipei, Taiwan
November 13 - 18, 2011

## Slide 2: Outline
Motivation
Goals
Proposal
  BW sub-TLVs
Examples
Discussion items
Summary & Next Steps
Backup

## Slide 3: Motivation
Address Flex-Grid needs in GMPLS:
Allow use of any combination of ‘Frequency Slots’
  Allocation of ‘Frequency Slots’ of different widths based on service needs (Modulation, Bit-rate)
  Slot overlap not allowed
Slot Width Granularity
  12.5 GHz × m where ‘m’ is a positive integer
Central Frequency Granularity
  6.35GHz

## Slide 4: Goals
A generic BW model that:
  covers all Super-Channel services
    Contiguous optical spectrum use
    Non-contiguous optical spectrum use (split-spectrum)
  covers potential evolution Flex-Grid standards
    Changes to slot-width, central frequencies
  ready for VCAT services

## Slide 5: Proposal
Simple extensions to ISCD [RFC 4202]
  Use a new Switching Capability
  Introduce Flex-Grid extensions in SCSI
Flex-Grid extensions summary
  Divide C-band spectrum in to ‘Slices’ of certain width
  Advertise ‘Slice’ availability
  Cover all 8-priorities
  Cover Min/Max ‘Frequency Slot’ use per LSP

## Slide 6: Slicing the C-band Spectrum
The usable spectrum is divided in to n-slices
Slice availability is advertised in BW-sub-TLV(s)
Slice Numbering is anchored @ N-Start
N-Start identifies start of usable spectrum supported by the advertising node
Slice Spacing is Single Slice granularity (e.g. 12.5GHz)

## Slide 7: Proposal: ISCD/SCSI formats
Switching Capability = Super Channel Switching Capable
SCSI to contain one or more BW-sub-TLVs (Type=1 or Type=2)

## Slide 8: Proposal: BW-sub-TLV(s)
Sub-TLV for List or Range option
Sub-TLV for Bit-map option

## Slide 9: Example: BW adv & Super-Channel LSPs
To create a Super Channel LSP over a single Flex-Grid link with
  Contiguous BW requirement = 200GHz (assume Transponder fully tunable)
The path computing node performs the following:
  Determine the number of slices required for the LSP (200/Slice-Spacing = 16)
  Look for contiguous spectrum availability on each link from BW adv (both dir)
    If available select the link for LSP creation.
Signal for LSP creation
Once created, update BW available using Bandwidth sub-TLV.

## Slide 10: Example: BW adv & Super-Channel LSPs cont’d
Consider a Te-Link that supports 4.8THz extended C-band
N-start = -142 (encode in 2’s complement)
Slice spacing = 12.5GHz (ref to Enumerated values in the draft)
Total number of slices available on the link = 384
Min SW field shows min consumption of 4 Slices per LSP ( =50GHz)
Max SW field shows up to 400GHz BW allowed per LSP (32x12.5GHz)

## Slide 11: CCAMP Mailing List Comments/Response
[Ramon Casellas] What will be the Max LSP BW for super channel
  [Abinder Nov04/2011] Max LSP BW is not really needed for super channel connection. All we need is max number of spectral slices which I am proposing in ISCD specific information. If we do want to show LSP BW in bps then we can convert spectral bandwidth of super channel into bps based on modulation.

## Slide 12: Summary & Next Steps
Re-using of existing ISCD definitions (RFC 4202)
Technology specific extensions consistent with GMPLS arch
Coverage for evolving Flex-Grid technology
  Different slice spacing, N-Start, Min/Max LSP BW
Coverage for all 8-priorities
Next Steps:
Discuss the requirements
Evaluate options

## Slide 13: Backup

## Slide 14: What is Super-Channel Connection
Multi-rate end to end connection on flex-grid
Realized with set of 12.5 GHz spectral slices
Spectral Slices can be contiguous or non-contiguous (split-spectrum super-channel)
Examples:
  Super Channel connection with spectral bandwidth of 200GHz ( 16 slices)
  Split-spectrum super-channel with spectral bandwidth of 250Ghz – 5 sets of slots of 50 GHz

## Slide 15: Example-3: If Type=2 TLV is used (ref to e.g. in slide-9)
Manipulate N-Start & N-End fields If Type=2 BW sub-TLV is used for adv of slices