## Slide 1: Generalized Label for Super-Channel Assignment on Flexible Grid
Iftekhar Hussain (ihussain@infinera.com)
Abinder Dhillon (adhillon@infinera.com)
Zhong Pan (zpan@infinera.com)
Marco Sosa (msosa@infinera.com)
Bert Basch (bert.e.basch@verizon.com)
Steve Liu (steve.liu@verizon.com)
Andrew G. Malis (andrew.g.malis@verizon.com)
draft-hussain-ccamp-super-channel-label-02
IETF 82 - Taipei, Taiwan
November 13 - 18, 2011

## Slide 2: New Co-Authors
  Bert Basch (bert.e.basch@verizon.com)
  Steve Liu (steve.liu@verizon.com)
  Andrew G. Malis (andrew.g.malis@verizon.com)

## Slide 3: Motivation
  Fixed Grid Limitations
  Future transport systems are expected to support data rates of 400 Gbps - 1 Tbps and beyond, using wider bandwidth optical channels
  ITU-T G.694.1 (fixed-grid ) permits allocation of channel spectrum bandwidth in "single" fixed- sized slots (e.g., 50GHz, 100GHz ) independent of the channel bit rate.
  This leads to inefficient use of optical spectrum due to excess frequency spacing for lower bit rate channels
  Flexible Grid Benefits
  FlexGrid allows allocation of “arbitrary” size channel spectral bandwidth as an integer multiple of 12.5 GHz fine granularity contiguous or non-contiguous slices depending on required channel bit rate
  This enables supporting multiple data rate super-channels in a spectrally efficient manner

## Slide 4: Super-Channel Label
Purpose
  A super-channel represents an ultra high aggregate capacity channel containing multiple carriers which are co-routed through the network as a single entity from the source transceiver to the sink transceiver
  This document defines a super-channel label format to setup an optical path manually or dynamically on a Flex-Grid network
Why?
  The existing label formats (e.g., RFC3471, RFC6205) either lack necessary fields to carry required flex-grid related information (e.g., channel spacing) or do not allow signaling of arbitrary flexible-size optical spectral bandwidth in an efficient manner (e.g., in terms of integer multiple of fine granularity slices)

## Slide 5: Super-Channel Label Format
Label Definition
  This document defines a super-channel label as consisting of a Super-Channel Identifier and an associated list of slices representing the optical spectrum of the super-channel
  Optical spectrum of a super-channel is flexibly enabled to be any subset of the slices (allows for split-spectrum super-channels)
  The slice spacing used is identified within the label and can take on multiple standard options, with default flex-grid slice spacing of 12.5GHz used here
Label Encoding Options
  Option A: Encode super-channel label as a list of start and end slice numbers corresponding to N slots (where a slot is a contiguous set of optical spectrum slices) with each slot denoted by its starting and ending slice number (N defaults to 1 for use of a single slot super-channel)
  Option B: Encode super-channel label as a first slice number of the grid (denoted as "n_start of Grid") plus the entire list of slices in the grid as a Bitmap where ‘1’ indicates inclusion of the slide in the super-channel

## Slide 6: Super-Channel Label Encoding Option A
Slice Spacing (e.g., 12.5 GHz)
Grid Type to be assigned by IANA (e.g., ITU-T Flex-Grid)
A logical identifier for a super-channel (similar to waveband Id defined in RFC3471)
The lowest or starting slice number of the slot # 1
The highest or ending slice number of the slot #1
Number of 32-bit entries in the super-channel label , where each entry is a contiguous slot of optical spectrum

## Slide 7: Super-Channel Label Encoding Option B
First slice number in optical Grid being referenced (i.e., the start of the left most edge of the Grid
For example n_start of Grid = -142 if the C-band left edge starts at 191.3250 THz using following formula:
Total number of slices in the grid
Each bit in the 32-bitmap word represents a particular slice with a value of 1 or 0 to indicate whether for that slice reservation is required (1) or not (0). Bit position zero in the first word represents the first slice in the Grid and corresponds to the value indicated in the “n_start of Grid” field

## Slide 8: Flexible Allowance of Split-Spectrum Super-Channel
Use Cases
  Avoid wasted bandwidth on fiber with fragmented BW due to super-channels with different spectral widths
    Enable faster restoration of optical bandwidth in these scenarios
  Enable super-channel to efficiently use both sides around a non-viable part of spectrum (e.g., lambda zero)
  Enable assignment of a single super-channel label for a set of (e.g., alien) disjoint wavelengths that may be defined for use between a pair of ports

## Slide 9: Super-Channel Label Example
  Assume the super-channel requires a spectral bandwidth of 200 GHz with left-edge frequency of 191.475 THz for the left-most 12.5 GHz slice and left-edge frequency of 191.6625 THz for the right-most slice
  n_start = (191.475 – 193.1)/0.0125 = -130
  n_end = (191.6625 – 193.1)/0.0125 = -115

## Slide 10: Comparison of Flex-Grid Drafts
 | draft-hussain-ccamp-super-channel-label-02 | draft-farrkingel-ccamp-flexigrid-lambda-label-01 | draft-zhang-ccamp-flexible-grid-rsvp-te-ext-00
Defines a new GMPLS label | Yes | Yes | No. Instead proposes to use RSVP Tspec to signal similar information
Encoding formats | Two options : Nx(start, end) and bitmap | Frequency (n) and spectrum width (m) | Frequency (n) and spectrum width (m)
Supports super-channels with contiguous spectrum | Yes | Yes | Yes
Supports split-spectrum super-channels | Yes | No | No
Flexibility to support networks with wavelength conversion | Yes | Yes | No (Since Tspec is end-to-end)