## Slide 1: Generalized Labels for the Flexi-Grid in Lambda-Switch-Capable (LSC) Label Switching Routers
A. Farrel, Old Dog Consulting
D. King, Old Dog Consulting
Y. Li, ZTE
F. Zhang, ZTE
R. Casellas, CTTC

## Slide 2: Motivation
The draft provides a “stake” in the ground for discussion of flexible grid labels.
  Builds on RFC6205 (Generalized Labels for Lambda-Switch-Capable LSRs).
This document was merged with draft-li-ccamp-flexible-grid-label.

## Slide 3: Label Format
Flexi-Label Encoding
  Currently extended to 64bits
  Slot Width “m” field (Slot Width (GHz) = 12.5 GHz * m)

## Slide 4: Open Items
Q1: Do we want a 64bit label or truncate at 40bits, or pad at 48bits?
  Might look more efficient to have shorter label.
  Label object is aligned on 32bit boundary anyway.
Q2: Do we use a new value for "Grid" or re-use DWDM value?
  We could go either way.
  It looks to us that it is slightly more helpful for implementation.
  Worth noting that:
    Grid value is not tied to any external SDO.
    Label type might be known from context anyway.
    It may be worth supporting fixed and flexi-grid in some hardware?

## Slide 5: Open Items, continued.
Q3: Is the "m" field part of the label, the traffic parameters, or both?
  We are only looking at label definition.
  Traffic parameter definition is also important.
  We feel that "m" is integral to the definition of the label.

## Slide 6: Summary & Next Steps
Overall, not an urgent piece of work.
  We must wait for Q6/15 in ITU-T.
  Deployment is not imminent.
Authors will continue to resolve outstanding questions/issues.
  Synch with other flexi-grid efforts.
At some point, we need to decide whether label should be in a separate I-D (modeled on RFC6205), or bundle all flexi-grid work together.