## Slide 1: OSPF-TE Protocol Extension for Constraint-aware RSA in Flexi-Grid Networks draft-zhangj-ccamp-flexi-grid-ospf-te-ext-00
J. Zhang, YL. Zhao, ZY. Yu
Beijing University of Posts and Telecommunications
82th IETF Taipei
Notes: <number>

## Slide 2
In flexi-grid networks, when processing routing and spectrum assignment (RSA) , some constraints need to be considered , such as spectral continuity constraint and impairments constraint.
In this draft, we consider two special constraints of flexi-grid :
Consecutive Spectrum Slots constraint
Variable Guard Band constraint
Motivation
Notes: <number>

## Slide 3: Consecutive Spectrum Slots Weight Information
It represents the situation of the available consecutive spectrum slots information in a link of the flexi-grid networks
For example the percentage of the total bandwidth of the number of five or ten consecutive spectrum slots...
Notes: <number>

## Slide 4: Variable Guard Band Information
It describes the guard band that between two adjacency client LSPs which is variable based on different network environments
It avoid crosstalk and bad impact that can affect the transmission performance of each client LSP
Notes: <number>

## Slide 5: OSPF-TE extension
Consecutive spectrum slots weight sub-TLV
Variable guard band sub-TLV
Notes: <number>

## Slide 6: Next Steps
Some other constraints to be considered?
Improve the document according to the feedback from meeting or mailing list
Comments are always appreciated
Notes: <number>

## Slide 7
Thank you